## Slide 1: BGP - Part 1
CS 168 – Fall 2017 – Section 11

## Slide 2: Administrivia
Project 3 due this Friday (11/17)

## Slide 3: Agenda
Interdomain Routing (BGP)

## Slide 4: BGP: Overview
Routing between ASes
AS = Autonomous System
  A “domain”
  Independently run network
  AT&T, UC Berkeley, Comcast, Google, etc.
    Companies, organizations, ISPs

## Slide 5: Interdomain Routing
ASes are autonomous
They want to…
  Choose their own internal routing protocol
    How to send packets within their domain
  Choose their own external policy
    E.g.: I don’t want to carry traffic directly from Google…
  Pick routes based on policies
  Keep policies private

## Slide 6: Three parts
eBGP
  Between border routers in different ASes
  Learn about external routes
iBGP
  Between border routers and other routers within a single AS
  Routers learn which border router to use for each external route
IGP
  The protocol used for intradomain routing (e.g. OSPF).
    Shortest path to subnet in the same AS
    Shortest path to border router for given external network
  Just a different name for L3 routing as we’ve talked about earlier

## Slide 7
The Big Picture
How does this fit with what we’ve learned so far?

## Slide 8
Host (you)
IP: 1.2.3.4
MAC: 01:0a:00:00:0b:02
Host
IP: 1.2.3.5
MAC: …
Host
IP: 1.2.3.6
MAC: …
Subnet (4th floor Soda)
1.2.3/24
L2: LAN
Destinations are MAC addresses
Learning switches
3rd floor Soda
1.2.4/24
7th floor Soda
1.2.5/24
Default gateway
Default gateway
Default gateway
LAN

## Slide 9
4th floor Soda
1.2.3/24
3rd floor Soda
1.2.4/24
7th floor Soda
1.2.5/24
L3: Intradomain
Destinations are IP addresses
IGP: exchange info about paths to local destinations
  DV routing and friends
Domain (AS)
UC Berkeley
IP prefix: 1.2/16
WAN: Intradomain

## Slide 10
4th floor Soda
1.2.3/24
3rd floor Soda
1.2.4/24
7th floor Soda
1.2.5/24
Domain (AS)
UC Berkeley
IP prefix: 1.2/16
Google
7.8/16
MIT
5.6/16
AT&T
3.4/16
WAN: Interdomain
Border router
Border router
Border router
Border router
Border router

## Slide 11
4th floor Soda
1.2.3/24
3rd floor Soda
1.2.4/24
7th floor Soda
1.2.5/24
Domain (AS)
UC Berkeley
AS number: 1
IP prefix: 1.2/16
Google (4)
7.8/16
MIT (3)
5.6/16
AT&T (2)
3.4/16
Interdomain: eBGP
Between border routers in different ASes
Learn about routes to external networks
Destinations are IP prefixes
5.6/16
Path: {3}
WAN: Interdomain

## Slide 12
4th floor Soda
1.2.3/24
3rd floor Soda
1.2.4/24
7th floor Soda
1.2.5/24
Domain (AS)
UC Berkeley
AS number: 1
IP prefix: 1.2/16
Google (4)
7.8/16
MIT (3)
5.6/16
AT&T (2)
3.4/16
Interdomain: eBGP
Between border routers in different ASes
Learn about routes to external networks
Destinations are IP prefixes
5.6/16
Path: {3,2}
WAN: Interdomain

## Slide 13
4th floor Soda
1.2.3/24
3rd floor Soda
1.2.4/24
7th floor Soda
1.2.5/24
Domain (AS)
UC Berkeley
iBGP
Intradomain: iBGP
Border routers and other routers within a single AS
To which border router should I send packets for MIT?

## Slide 14: Soda 4th Floor  MIT
4th floor Soda
Default gateway
Border router
Border router
Default gateway
2nd floor CSAIL
UC Berkeley
MIT
LAN
LAN
ASes

## Slide 15: In the end…
Host knows how to…
  ... get to the default gateway on its local subnet
Default gateway knows how to...
  ... get to the right border router
Border router knows how to...
  ... get to the right AS
AS knows how to...
  ... get to the right internal host

## Slide 16: Today
The routing mechanics
We will not talk about specific policies…
  For next section

## Slide 17: Similarities between BGP & DV routing
Destination based
No global view of network
Iterative and distributed convergence

## Slide 18: Differences between BGP & DV routing
May choose path that is not the shortest
  Base choices on policy instead
Path vector
  Don’t send distance, send path
  Crucial for avoiding loops
Route aggregation
  Combine network prefixes when possible
Selective route advertisement
  Don’t have to send updates to all neighbors

## Slide 19: Not Picking Shortest Route
AT&T
(1)
Facebook
(2)
Google
(3)
AT&T may pick path {1, 2, 3} over {1, 3}

## Slide 20: Path Vector
AS 1 1.2/16
AS 2
AS 3
1.2/16
Path: {1}
1.2/16
Path: {2,1}

## Slide 21: Path Vector Benefits
Loop avoidance
  How?
  Don’t use a path we’re already on
Allows for flexible policies
  AS can avoid paths through certain other ASes, countries, etc.

## Slide 22: Route Aggregation
Combine prefixes
   Scalability
AT&T
1.0.0.0/8
UC Berkeley
1.2/16
Stanford
1.3/16
Google
1.4/16
1.0.0.0/8
This way!
dst: 1.4.5.6
dst: 1.3.4.5

## Slide 23: Selective Route Advertisement
AS may advertise routes to only some neighbors
  Based on policies
AT&T
Facebook
Google

## Slide 24: Selective Route Advertisement
E.g. Facebook might not want to carry traffic between AT&T and Google
  Don’t tell AT&T about path to Google
  Don’t tell Google about path to AT&T
AT&T
Facebook
Google

## Slide 25: Export & Selection
Export: Choose which routes to advertise
  Determines where AS will receive traffic from
  Which traffic to carry
Selection: Choose route advertisements to accept
  Determines where AS will send traffic

## Slide 26: Export & Selection
UC Berkeley
AT&T
Google
Comcast
Facebook
Stanford this way!
Stanford this way!
UCB and Facebook export their route to Stanford
They agree to carry AT&T’s traffic to Stanford

## Slide 27: Export & Selection
UC Berkeley
AT&T
Google
Comcast
Facebook
Stanford this way!
AT&T selects route through UC Berkeley
AT&T might now send traffic to Stanford via UCB

## Slide 28: Export & Selection
UC Berkeley
AT&T
Google
Comcast
Facebook
Stanford this way!
AT&T exports route to Google only
Agrees to carry Google’s traffic to Stanford, but not Comcast’s

## Slide 29
Worksheet