## Slide 1: Packets in Flight
CS 168 – Fall 2017 – Section 2
Notes: V1: Ankit Mathur

## Slide 2: Delays
How long does it take for your data to reach its destination?
It depends on…
  how much data you’re sending and the link speed  transmission delay
  your distance from the destination  propagation delay
  the traffic pattern  queuing delay
  how fast routers process the packet header  processing delay
Notes: Transmission – how long it takes computer to actually put bits onto the wire. Depends on how much data you’re sending and the link speed
Propagation – normally speed of light.
Queueing – the traffic pattern. Routers are usually receiving/sending many packets on many different connections simultaneously, and this can slow down the network.

## Slide 3: Delays
How long does it take for your data to reach its destination?
It depends on…
  how much data you’re sending and the link speed  transmission delay
  your distance from the destination  propagation delay
  the traffic pattern  queuing delay
  how fast routers process the packet header  processing delay
Notes: Processing – not really gonna talk about them

## Slide 4: Transmission Delay
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
Notes: test

## Slide 5: Transmission Delay
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
  Limited by the bandwidth
Notes: Bandwidth – how many bits you can send through a wire per second

## Slide 6: Transmission Delay
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
  Limited by the bandwidth
  Function of packet size
Notes: Transmission delay depends on packet size: the more data you have to send, the longer it’s gonna take to put that data onto the wire. You can only put so many bits onto the wire per second

## Slide 7: Transmission Delay
Notes: Transmission delay depends on packet size: the more data you have to send, the longer it’s gonna take to put that data onto the wire. You can only put so many bits onto the wire per second

## Slide 8: Transmission Delay: Example
Packet size = 500B
Bandwidth = 4 Mbps

## Slide 9: Transmission Delay: Example
Packet size = 500B
Bandwidth = 4 Mbps

## Slide 10: Propagation Delay (latency)
How long it takes to transmit one bit from one end to the other
Depends on the length of the link
Limited by the speed of light (propagation speed of link)
Does NOT depend on the size of the packet

## Slide 11: Propagation Delay: Formula

## Slide 12: Propagation Delay: Example

## Slide 13: Bandwidth Delay Product (BDP)
Now that we know the propagation delay, we can tell how many bits are “in flight” (on the link) at any time
??
??
BDP = ?? * ??

## Slide 14: Bandwidth Delay Product (BDP)
Now that we know the propagation delay, we can tell how many bits are “in flight” (on the link) at any time
Bandwidth
Propagation delay

## Slide 15
Packets might have to wait before they can be transmitted…

## Slide 16: Queuing Delay
How long the packet waits to get transmitted on the wire
Happens when arrival rate is greater than transmission rate

## Slide 17: An easy fix for queuing delay?
Naïve solution: max(arrival rate, receive rate)
Is this sufficient?

## Slide 18: Burstiness!
Transmission rate = constant over time
Arrival rate = not constant over time
Netflix Traffic, circa 2010

## Slide 19: Burstiness and Queues
How does burstiness affect queuing delays?
What happens when the queue is full?

## Slide 20: Queues
How does burstiness affect queuing delays?
  Bursty flows tend to increase queuing delay
What happens when the queue is full?
  Packets are dropped

## Slide 21: End-to-End Delay
Sum of all nodal delays on the path

## Slide 22: Round Trip Time (RTT)
The time it for the packet to reach its destination and receive a response

## Slide 23: Visualizing packet delay…
Transmission delay
Propagation delay
Time

## Slide 24: Visualizing end-to-end delay…
Transmission delay
Propagation delay
Transmission delay
Propagation delay
A
R
B
Time

## Slide 25: Visualizing end-to-end delay…
Transmission delay
Propagation delay
Transmission delay
Propagation delay
What is this??
Two packets, back-to-back
End-to-end delay of brown packet
Time

## Slide 26: Visualizing end-to-end delay…
Queuing delay
Time
Two packets, back-to-back
End-to-end delay of brown packet
Transmission delay
Propagation delay
Transmission delay
Propagation delay