## Slide 1: All About Routing
CS 168 – Fall 2017 – Section 3

## Slide 2: Agenda
Ethernet Forwarding (L2)
  Simple learning switches
  Spanning tree protocol
Network (L3)
  Link-state routing
Transport
Network
Datalink
Physical
Application

## Slide 3: Forwarding
A packet with (source, destination) arrives at a switch
Where should the switch send the packet?
2
3
4
SRC | DEST
A | D
Packet Header
1
?
?
?

## Slide 4: Forwarding
The switch checks its forwarding table
  Maps dest -> outgoing link
2
3
4
SRC | DEST
A | D
Packet Header
DEST | OUTGOING LINK
A | 1
D | 3
B | 2
1

## Slide 5: Forwarding
If the dest is found, send out that link!
2
3
4
SRC | DEST
A | D
Packet Header
1
DEST | OUTGOING LINK
A | 1
D | 3
B | 2
DEST | OUTGOING LINK
A | 1
D | 3
B | 2

## Slide 6: Forwarding
What if the dest is not found?
  Could drop, flood, etc.
2
3
4
Packet Header
1
SRC | DEST
(ˆ(oo)ˆ) | ᄽὁȍ ̪őὀᄿ
DEST | OUTGOING LINK
A | 1
D | 3
B | 2
Notes: Pig and spider

## Slide 7: Recall…
What makes a routing state valid?
For every destination:
  If all paths to that destination have:
    No dead-ends (except destination)
    No loops
Then the state is valid

## Slide 8: Spanning Trees
One way to solve loops:
  Use a topology that doesn’t have any!
Spanning Tree
  Used by Ethernet networks (L2)
Notes: SPT protocol later, first talk about learning switches

## Slide 9: Learning Switches
What if the dest is not found?
  Flood!
    In a spanning tree, this won’t cause loops
DEST | OUTGOING LINK
D | 3
B | 2
A
A
SRC | DEST
(ˆ(oo)ˆ) | ᄽὁȍ ̪őὀᄿ
ᄽὁȍ ̪őὀᄿ
1
3
2
4
Wilbur’s in trouble!
I don’t care
I don’t care
I don’t care
I don’t care
(ˆ(oo)ˆ)

## Slide 10: Learning Switches
What if the dest is not found?
  Flood!
    In a spanning tree, this won’t cause loops
We also learn where the src is!
DEST | OUTGOING LINK
A | 1
D | 3
B | 2
A
A
SRC | DEST
(ˆ(oo)ˆ) | ᄽὁȍ ̪őὀᄿ
ᄽὁȍ ̪őὀᄿ
1
3
2
4
DEST | OUTGOING LINK
D | 3
B | 2
(ˆ(oo)ˆ) | ?
(ˆ(oo)ˆ)

## Slide 11: Learning Switches
What if the dest is not found?
  Flood!
    In a spanning tree, this won’t cause loops
We also learn where the src is!
A
A
SRC | DEST
(ˆ(oo)ˆ) | ᄽὁȍ ̪őὀᄿ
ᄽὁȍ ̪őὀᄿ
1
3
2
4
DEST | OUTGOING LINK
D | 3
B | 2
(ˆ(oo)ˆ) | 1
(ˆ(oo)ˆ)

## Slide 12: Learning Switch: Pseudocode
When a learning switch receives a packet:
Lookup the DEST in the switch table
if entry found for destination {
if dest on link from which packet arrived then drop packet
else forward packet on link indicated
}
else flood
Notes: Inner if statement is used to prevent routers from being “locally stupid” and causing a back-and-forth loop

## Slide 13: Spanning Tree Protocol (STP)
Goal:
  To make this network…

## Slide 14: Spanning Tree Protocol (STP)
Goal:
  To make this network…
  Function like this!

## Slide 15: Spanning Tree Protocol (STP)
Algorithm in two parts:
  Pick a root (by smallest Ethernet address)
  Compute shortest paths to that root
    Only keep the links on the shortest paths
    Break ties by neighbor with smaller address
Notes: Tie: if I get 2 messages with the same root and distance, one from router 3, the other one from router 4
-I choose the message/route given by router 3

## Slide 16: Spanning Tree Protocol (STP)
Each router sends a message to its neighbors
  (I think 4 is the root. My distance to 4 is 0. I am 4. )
    Root, Distance, Src
When routers receive a message, they update their current knowledge of the root and distance to it.
  If 4 receives (3, 0, 3):
    It will now think (3 is the root. My distance is 1. I am 4.)
Repeat until everyone agrees

## Slide 17: The Spanning Tree Battlefield
Day 1
2
1
3
4
5
6

## Slide 18: The Spanning Tree Battlefield
Day 2
2
1
3
4
5
6
Notes: Note: what if there was a link between router 2 and 3?
-Router 2 links to router 3 instead of router 5 (due to tiebreaker)

## Slide 19: The Spanning Tree Battlefield
Day 3
2
1
3
4
5
6
Notes: Note: what if there was a link between router 2 and 3?
-Router 2 links to router 3 instead of router 5 (due to tiebreaker)

## Slide 20: The Spanning Tree Battlefield
Day 4: 1 Wins!
2
1
3
4
5
6

## Slide 21: The Spanning Tree Battlefield
Now the links form a spanning tree...
And we can deploy our learning switches and flood!

## Slide 22
Any questions?

## Slide 23: Routing in the Network (L3)
Goal: Compute the shortest routes
for all (source -> destination) pairs
Two main algorithms we‘ll discuss:
Link State Routing
  Calculate on global topology
Distance Vector Routing
  Project 2, out soon™!
  Next section...
Transport
Network
Datalink
Physical
Application

## Slide 24: Link State Routing
Routers share info about their local neighbors
Together, they learn the global topology
Then compute the shortest paths themselves!
  With Dijkstra‘s, etc.
4
2
1

## Slide 25: Link State Routing
Routers share info about their local neighbors
Together, they learn the global topology
Then compute the shortest paths themselves!
  With Dijkstra‘s, etc.
4
1
2