## Slide 1: Distance-Vector Routing
CS 168 – Fall 2017 – Section 4

## Slide 2: Agenda
Network (L3)
  Distance-Vector Routing
Transport
Network
Datalink
Physical
Application

## Slide 3: Distance-Vector Key Points
Scalable
  Unlike link-state, routers don’t need global network topology
Distributed
  Routers communicate with neighbors to compute routes
Minimizes Distance
  Avoids loops and minimizes “cost,” not necessarily physical distance

## Slide 4: Distance-Vector Routing
Each router…
  Has a “vector” of distances to each destination
  Also keeps track of next-hop router for each destination
  Uses its own outgoing link costs to compute its initial vector
B
D
A
7
2
C
16
9
Initial State
A | B | C
0, A | 2, B | 9, C
A | B | C | D
9, A | 1, B | 0, C | 16, D
A | B | C | D
2, A | 0, B | 1, C | 7,D
B | C | D
7, B | 16, C | 0, D
1

## Slide 5: Two Components of Distance-Vector
Protocol
  Each router floods its vector to neighbors when helpful
Algorithm
  - Upon receiving a vector from a neighbor, each router uses Bellman-Ford to update its own vector

## Slide 6: Protocol
Each router advertises its vector to all of its neighbors
Whenever any distance to a destination changes in its vector
- Including when it builds its initial vector
2. Periodically
- Helps with consistency among neighbors

## Slide 7: Protocol Example
Since each router just built its initial vector, each of them advertises its vector by flooding
  Only A is shown here, but B,C,D do the same
B
D
A
7
2
C
16
9
A | B | C
0, A | 2, B | 9, C
B | C | D
7, B | 16, C | 0, D
1
A | B | C | D
2, A | 0, B | 1, C | 7,D
A | B | C | D
9, A | 1, B | 0, C | 16, D

## Slide 8: Algorithm
Upon receiving a vector from its neighbor, a router:
  Learns about new destinations
  Uses Bellman-Ford to update its vector
    for d in destinations:
    minCost, nextHop = ∞, None
    for n in neighbors:
    c = cost of link to n
    a = advertised distance from n to d
    if a + c < minCost:
    minCost = a + c
    nextHop = n
    vector[d] = (minCost, nextHop)
  Flood vector if any entry changed!

## Slide 9: Distance-Vector Walkthrough
Continuing the example from earlier
Let’s consider just router A for now
All routers initially flood their vectors
B
D
A
7
2
C
16
9
A | B | C
0, A | 2, B | 9, C
B | C | D
7, B | 16, C | 0, D
1
A | B | C | D
2, A | 0, B | 1, C | 7,D
A | B | C | D
9, A | 1, B | 0, C | 16, D

## Slide 10: Walkthrough
Initially, A doesn’t know either of its neighbors’
vectors
A
A | B | C
0, A | 2, B | 9, C
B’s vector
A’s Perspective
?
C’s vector
?
B
D
A
7
2
C
16
9
1
A’s vector

## Slide 11: Walkthrough
A receives B’s vector
  - Learns about D
  Using Bellman-Ford, updates its entries for dests C and D
  - Floods new vector to neighbors
A
A | B | C
0, A | 2, B | 9, C
A | B | C | D
2, A | 0, B | 1, C | 7,D
B’s vector
C’s vector
?
A
A | B | C | D
0, A | 2, B | 3, B | 9, B
A | B | C | D
2, A | 0, B | 1, C | 7,D
B’s vector
C’s vector
?
B
D
A
7
2
C
16
9
1
A’s vector
A’s vector

## Slide 12: Walkthrough
A receives C’s vector
  Using Bellman-Ford, realizes it has no updated distances
  - Does not flood vector to neighbors
A
A | B | C | D
2, A | 0, B | 1, C | 7,D
B’s vector
C’s vector
A
A | B | C | D
0, A | 2, B | 3, B | 9, B
A | B | C | D
2, A | 0, B | 1, C | 7,D
B’s vector
C’s vector
A | B | C | D
9, A | 1, B | 0, C | 16, D
A | B | C | D
9, A | 1, B | 0, C | 16, D
B
D
A
7
2
C
16
9
1
A’s vector
A | B | C | D
0, A | 2, B | 3, B | 9, B
A’s vector

## Slide 13: Walkthrough
Eventually all vectors will converge
  Routers still send periodic updates to deal with network changes
B
D
A
7
2
C
16
9
A | B | C | D
0, A | 2, B | 3, B | 9,B
A | B | C | D
3, B | 1, B | 0, C | 8, B
A | B | C | D
2, B | 0, B | 1, B | 7,B
A | B | C | D
9, B | 7, B | 8, B | 0,D
1

## Slide 14: Special Case 1: Poison Reverse
A realizes C is its first hop router to D, as well as to C…
  A changes its distance to D and C to infinity
  Sends this modified vector to C
A
C
A | B | C | D
0, A | 2, B | 2,C | 4, C
B
D
D
2
A | B | C | D
0, A | 2,B | 2, C | ∞
2
2

## Slide 15: Special Case 2: Split Horizon
Split horizon is the same as poison reverse, except…
  In split horizon, A does not advertise its distance to D and C at all when sending its vector to C
  Similarly, A does not advertise its distance to B when sending its vector to B
A
C
B
D
2
2
2
A | B
0,A | 2,B
A | C | D
0,A | 2,C | 4,C

## Slide 16: Special Case 3: Route Poisoning
When a link between A and C goes down and they can no longer reach each other…
  A advertises infinity for dest C, and vice versa
  A also advertises infinity to D because A uses C to get to D (same with C to B)
A
C
A | B | C | D
0, A | 2,B | ∞ | ∞
B
D
D
2
2
A | B | C | D
∞ | ∞ | 0, C | 2, D

## Slide 17: Combinations of Strategies
Route Poisoning + Poison Reverse
  Efficient updates
Split Horizon + Poisoning
  Only split horizon means full update required on link going down
  Only poisoning means have to explicitly send poison for every route don’t have

## Slide 18: Diagram for Q1

## Slide 19: LOST Session
(Lost and Overwhelmed Student's Turnabout) 
Safe space for students who feel like they have lost contact with the class and need help reconnecting with one or more of the basic concepts
320 Soda, Friday 5-6 PM
We encourage checking it out if you’re feeling on shaky ground!