## Slide 1: DHCP and ARP
CS 168 – Fall 2017 – Section 7

## Slide 2: Agenda
DHCP (Application)
ARP (Datalink)
Transport
Network
Datalink
Physical
Application

## Slide 3: Big-Picture Question
How does a host send a packet to another host?
Today’s section will bring us much closer to the answer

## Slide 4: DHCP
Enables a host to learn about its….
  Own IP Address
  Network Mask
  First-hop router’s IP Address
  DNS Server(s) IP Address(es) (more on this next week..)
INTERNET
?
?
?
?
?
?
?

## Slide 5: Preliminary Questions
Difference between flooding and broadcasting?
  Flooding has the goal of host-to-host delivery
    A per-hop decision
    What I do with a packet when I don’t know what to do with it
  Broadcast has the goal of delivery to everyone
    How I specify that my packet will go to everyone
How does DHCP broadcast at L2 layer?
  DHCP does not know about L2 addresses!
  DHCP specifies destination IP address as 255.255.255.255
  - Link-layer then uses MAC address ff:ff:ff:ff:ff:ff

## Slide 6: DHCP
DHCP server(s) located on same local network as host
Host initially broadcasts discovery message
Local Network
DHCP Server
IP Address: ???
Subnet Mask: ???
First-hop Router IP Address: ???
DNS IP Address: ???

## Slide 7: DHCP
DHCP server(s) responds by broadcasting offer message
Message includes assigned IP address, network mask, first-hop router address, DNS server addresses
Local Network
DHCP Server
IP Address: ???
Subnet Mask: ???
First-hop Router IP Address: ???
DNS IP Address: ???
IP Address: 212.0.0.0 (tentative)
Subnet Mask: /8 (tentative)
First-hop Router IP Address: 212.2.3.0 (tentative)
DNS IP Address: 212.4.7.8 (tentative)

## Slide 8: DHCP
Host responds by broadcasting request message
This message identifies which offer was accepted (helps when there are multiple local DHCP servers)
Local Network
DHCP Server
IP Address: 212.0.0.0 (tentative)
Subnet Mask: /8 (tentative)
First-hop Router IP Address: 212.2.3.0 (tentative)
DNS IP Address: 212.4.7.8 (tentative)

## Slide 9: DHCP
Chosen DHCP server responds by broadcasting ACK
Local Network
DHCP Server
IP Address: 212.0.0.0 (confirmed!)
Subnet Mask: /8 (confirmed!)
First-hop Router IP Address:212.2.3.0 (confirmed!)
DNS IP Address: 212.4.7.8 (confirmed)
IP Address: 212.0.0.0 (tentative)
Subnet Mask: /8 (tentative)
First-hop Router IP Address: 212.2.3.0 (tentative)
DNS IP Address: 212.4.7.8 (tentative)

## Slide 10: A Couple Questions….
1. Dealing with failures?
  Hosts have a lease periods for their IP addresses
  Hosts must refresh before lease period ends
Why do we need the first-hop router’s IP address and the subnet mask?
  - Answered when we talk about ARP.

## Slide 11: ARP (Overview)
When host sends packet, needs to specify dest MAC address so packet can traverse local networks
Each host has ARP table, which maps IP to MAC
If mapping unknown, ask local network by broadcasting “Who has IP address x?”
  Host with IP x responds “My MAC is y”
Local Network
Dest Host
IP: a.b.c.d
MAC: 11:11:11:11:11:11
IP Addr. | MAC Addr.
a.b.c.d | 11:11:11:11:11:11
a.b.c.a | 12:37:11:11:11:11
ARP Table

## Slide 12: ARP (Within local network)
Destination is in same local network
Use ARP table to lookup MAC address of dest
Specify MAC address when sending packet
Local Network
Dest Host
IP: a.b.c.d
MAC: 11:11:11:11:11:11
IP Addr. | MAC Addr.
a.b.c.d | 11:11:11:11:11:11
a.b.c.a | 12:37:11:11:11:11
ARP Table
Src Host

## Slide 13: ARP (Across local networks)
Destination is NOT in same local network
How can we tell?
  Use subnet mask to check dest network address
Local Network 1
IP Addr. | MAC Addr.
d.c.b.a | 22:11:11:11:11:11
d.c.b.c | 12:37:11:11:11:11
ARP Table
Src Host
Local Network 2
Src’s First Hop Router
IP: d.c.b.a
MAC: 22:11:11:11:11:11
Dest Host
IP: a.b.c.d
MAC: 11:11:11:11:11:11

## Slide 14: ARP (Across local networks)
Use ARP table to lookup MAC address of first-hop-router (which is in same local network)
  We know router’s IP address through DHCP!
Specify first-hop router’s MAC address in packet and send packet
Local Network 1
IP Addr. | MAC Addr.
d.c.b.a | 22:11:11:11:11:11
d.c.b.c | 12:37:11:11:11:11
ARP Table
Src Host
Local Network 2
Src’s First Hop Router
IP: d.c.b.a
MAC: 22:11:11:11:11:11
Dest Host
IP: a.b.c.d
MAC: 11:11:11:11:11:11

## Slide 15: ARP (Across local networks)
First-hop router will route packet to router 2 using dest IP address
  Dest IP address is a.b.c.d. in this example
  Detail: Routers also use ARP to discover each another router’s MAC address, if they initially have nothing in their ARP cache.
Local Network 1
IP Addr. | MAC Addr.
d.c.b.a | 22:11:11:11:11:11
d.c.b.c | 12:37:11:11:11:11
ARP Table
Src Host
Local Network 2
Src’s First Hop Router
IP: d.c.b.a
MAC: 22:11:11:11:11:11
Dest Host
IP: a.b.c.d
MAC: 11:11:11:11:11:11

## Slide 16: ARP (Across local networks)
Router 2 will use its ARP table to reencapsulate packet’s dest MAC address with actual dest host’s MAC address
  Router 2 then sends packet to dest host
Local Network 1
IP Addr. | MAC Addr.
d.c.b.a | 22:11:11:11:11:11
d.c.b.c | 12:37:11:11:11:11
ARP Table
Src Host
Local Network 2
Src’s First Hop Router
IP: d.c.b.a
MAC: 22:11:11:11:11:11
Dest Host
IP: a.b.c.d
MAC: 11:11:11:11:11:11
IP Addr. | MAC Addr.
a.b.c.d | 11:11:11:11:11:11
a.b.c.c | 17:33:33:33:11:11
ARP Table

## Slide 17: What are we missing?
How do we determine destination IP address?
  Will cover in DNS