## Slide 1: TCP
CS 168 – Fall 2017 – Section 9

## Slide 2: Agenda
Transmission Control Protocol (TCP)

## Slide 3: TCP
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
L4 Protocol (Transport)
Byte Stream
Bi-directional
Reliable
In-order
Notes: UDP is message-oriented
Message Oriented protocols send data in distinct chunks or groups. Stream protocols send a continuous flow of data.

## Slide 4: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Host port numbers
  Multiplexing and demultiplexing
  16 bits

## Slide 5: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Byte offset
  Of first payload byte
  Initialized randomly
Byte Stream Protocol
  Seq # refers to bytes
Notes: If the SYN flag is set (1), then this is the initial sequence number. The sequence number of the actual first data byte and the acknowledged number in the corresponding ACK are then this sequence number plus 1.
If the SYN flag is clear (0), then this is the accumulated sequence number of the first data byte of this segment for the current session.
Bytes rather than packets

## Slide 6: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Cumulative ACKs
Seq # of next byte
Data packets carry ACKs

## Slide 7: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Header length
  4 bits
  In 4-byte words
Minimum 5 words (20 B)
Maximum 15 words
  Why?
Notes: Only 4 bits, so max is 2^4 – 1 = 15 words

## Slide 8: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
SYN
  SYNchronize initial state
ACK
  ACKnowledgement
FIN
  No more data
RST
  Connection ReSeT
Notes: 9 bits
FIN says "i finished talking to you, but i'll still listen to everything you have to say until you're done"
RST says "there is no conversation. i won't say anything and i won't listen to anything you say
If the SYN flag is set (1), then this is the initial sequence number. The sequence number of the actual first data byte and the acknowledged number in the corresponding ACK are then this sequence number plus 1.
If the SYN flag is clear (0), then this is the accumulated sequence number of the first data byte of this segment for the current session.

## Slide 9: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Receive Window Size
  Maximum receiver buffer
Limits sending rate
  Don’t send faster than receiver can process
Notes: unit: byte
limited to between 2 and 65,535 bytes.

## Slide 10: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Checksum
  Includes header and payload
Options common
  Unlike IP
  Not covered
  Assume no options unless specified

## Slide 11
Connection Establishment

## Slide 12: Connection Establishment
Sequence number and acknowledgement number don’t start from zero
Instead client and server choose a random initial seq #
  Why?
Must be communicated between client and server
Notes: Connection spoofing, connection resetting, and data injection

## Slide 13: Connection Establishment
Client/Server exchange state
  Initial Sequence numbers
  Port number
  TCP Options
Notes: example about TCP options:
- Maximum Segment Size (MSS)
- Selective Acknowledgements (SACK)

## Slide 14: Three Way Handshake
Client sends server a SYN
  A TCP packet with the SYN flag set
SYN packet carries initial state
  Receive window
  Source port number
  Initial sequence number

## Slide 15: Three Way Handshake
Server responds with a SYN-ACK
Acknowledge the client’s SYN
Respond with the server’s own SYN
Carries server’s initial state
  Receive window
  Source port number
  Initial sequence number

## Slide 16: Three Way Handshake
Client responds with an ACK
Now the connection is established!
  Client and server can freely communicate

## Slide 17
Teardown

## Slide 18: Two Teardown Methods
Four way handshake
  Graceful/normal teardown
Reset
  Exceptional Teardown

## Slide 19: Normal Teardown
One side closes their connection
  Indicates they will send no more data
  Sends a FIN
  Receives an ACK
Other side may continue transmitting
Eventually it closes as well
  Sends a FIN
  Receives an ACK
Connection is closed
Notes: could combine into three-way handshake

## Slide 20: TCP Reset
Reset the connection
  Most commonly, attempt to SYN on a closed port
Send RST packet(s) only (no ACK)
Notes: If side that sent RST receives more packets, will resend the RST

## Slide 21
Reliability

## Slide 22: Reliability
Cumulative ACKs
  Allow detection of dropped packets
How do we know a packet was lost?
  Timeout
  Duplicate ACKs

## Slide 23: Timeout
Retransmission Time Out (RTO)
  Timeout after which packets are retransmitted
  Based on a constantly updated RTT estimate (and variance)
Single timer (not per-packet)
  Each received ACK resets RTO
  If RTO times out
    Retransmit packet containing “next byte”
Notes: exponential weighted moving average

## Slide 24: Timeout
What if RTO is too large?
Packet is dropped . . .
  Wait
  Keep waiting
  … Keep waiting
  Timer goes off
    Finally retransmit
Can we do better?

## Slide 25: Duplicate ACKs
Transmit
  Seq 1000
  Seq 2000
  Seq 3000 Dropped in flight
  Seq 4000
  Seq 5000
  Seq 6000
What ACKs do we receive?
  ACK 2000
  ACK 3000
  ACK 3000
  ACK 3000
  ACK 3000
Duplicate ACKs indicate packet loss/reorder