## Slide 1: CS 168 Forwarding
Fall 2016
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Last Lecture (1)
Requirements for addressing:
  Efficient Forwarding: Fast lookup
  Scalable Routing: Compact state exchanges
  E2E Check: Know that packets are for me
Scalable addressing schemes: ideal, not real
  L2: Switch : MAC
  L3: AS : Network : Host
But that’s not what we use….
  L2: just MAC L3: Network/Host (sort of)

## Slide 4: Last Lecture (2)
IP addresses
  dot quad notation 16.45.231.117
  slash notation: /8 means first 8 bits are network address
History of addressing schemes
  Original IP: Network (8 bits) : Host (24 bits)
  Classful: first few bits specify length of network address
  CIDR: use mask to denote length of network address
    Informally, just use slash notation

## Slide 5: Last Lecture (3)
Hierarchy in delivery:
L3: handles delivery between networks
L2: handles delivery to hosts within network
Separation of concerns:
Routers only route based on network address
L2 only cares about the host address (and MAC)
Finding addresses:
DNS (later) maps names to IP addresses
ARP (later) turns IP addresses into MAC

## Slide 6: Last Lecture: What I Wish I’d Said
With original IP addressing, routing algorithms exchanges network addresses as destinations
  “I have a five hop path to this network”
  And routing tables were list of network addresses
With CIDR, what does a routing algorithm advertise (and route on)?
  Network addresses, right?
  Not really….
When you aggregate two network addresses, what do you get?
  A prefix!

## Slide 7: What is a prefix?
A prefix is something you use to route packets
It is a bit subset of one or more network addresses
I can hear you all thinking “what the @#$@#?”
But just hold on…

## Slide 8: Aggregation
When I have two contiguous network addresses being routed to the same output port, I would like to use only one routing entry
The routing entry is not itself a network address
  It is a shared prefix!
  It must match each aggregated network address
  It must thus be shorter than each of them (why?)
A prefix matches one or more network addresses that go to the same output port

## Slide 9: Example
Assume that we have two networks:
  201.10.4/24 and 201.10.5/24
  These are physical L2 networks with these addresses
Routing table in some internal router has:
  201.10.4/24  Port 3
  201.10.5/24  Port 3
What is a more efficient representation?

## Slide 10: Cheat Sheet
201.10.4/24=11001001|00001010|00000100|*******
201.10.5/24=11001001|00001010|00000101|*******
201.10.4/23=11001001|00001010|0000010*|*******
This is their shared prefix…
More efficient representation?
  201.10.4/23  Port 3

## Slide 11: In CIDR
Routing entries are prefixes
These prefixes summarize the routing of all network addresses
Aggregation allows you to condense multiple routing entries into one
  Contiguous (have shared prefix)
  Go to same destination
I did not yet say that no one else shares that prefix
  Let me avoid that detail for now….

## Slide 12: Why Prefixes So Important to CIDR?
One can have prefixes as compressed routing entries in any addressing scheme
  Though in some aggregation may be unlikely
But one of the main points of CIDR was to encourage aggregation.
In CIDR one cannot tell the difference between network addresses and prefixes, so their use is more natural and ubiquitous.
  In CIDR, if you hand me a prefix, I can’t tell if this represents one network address or many…

## Slide 13: Questions?

## Slide 14: Aggregation (and not)

## Slide 15: Scalability via Address Aggregation
Provider is given 201.10.0.0/21 (201.10.0.x .. 201.10.7.x)
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider
Routers in the rest of the Internet just need to know how to reach 201.10.0.0/21. The provider can direct the IP packets to the appropriate customer.
Each customer
given smaller prefix

## Slide 16: Global Picture
201.10.0/21Port 1
201.11.0/21Port 2
202/8 Port 4
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP
Only /21 listed in core
/22, /23, /24 only listed in ISP’s router
Notes: If adfertised separtely, would have to change whenever prefixes changed. Added new customer, split old one….

## Slide 17: Prefix Aggregation
Original Prefix:
201.10.0/21=11001001|00001010|00000***|*******
Subprefixes: (disjoint coverage of original prefix)
201.10.0/22=11001001|00001010|000000**|*******
201.10.4/24=11001001|00001010|00000100|*******
201.10.5/24=11001001|00001010|00000101|*******
201.10.6/23=11001001|00001010|0000011*|*******

## Slide 18: Aggregation Not Always Possible
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homed customer with 201.10.6.0/23 has two providers. Other parts of the Internet need to know how to reach these destinations through both providers.
 /23 route must be globally visible
Notes: What does core route do now????

## Slide 19: Multihoming Global Picture
201.10.0/21Port 1
201.10.6/23Port ?
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
(1) Which ISP does core send 201.10.6/23 to?
It depends on factors besides addressing…..
If 201.10.6/23  Port 1 no need to list separately
If 201.10.6/23  Port 2 must list separately
Which raises two questions….

## Slide 20: Addresses Advertised in Two Places?
Provider 1 and Provider 2 both advertise prefix
  That is, they both claim they can reach prefix
What problems does this cause?
  None, in terms of basic connectivity!
DV: routers often offered two paths to destination
  Pick the shorter path
For interdomain routing, other factors matter:
  Policy, nature of commercial relationship, prefix length
We will return to this example….
  Focus now on multihoming as impediment to aggregation

## Slide 21: Multihoming Global Picture
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
(2) What if we have contradictory entries in routing table?

## Slide 22: What’s the Problem?
Packets in 201.10.6/23 match two conflicting entries!
  Every address in 201.10.6/23 is also in 201.10.0/21
Which entry do we use?
We will answer this after a digression into forwarding
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..

## Slide 23: Questions?

## Slide 24: Forwarding
Caveat: I’ve never seen a real network, nor a real router, so this is all just hearsay!

## Slide 25: Networks and routers
AT&T
BBN
NYU
UCB
core
core
edge (ISP)
edge (enterprise)
home, small business
Notes: Bunch of different kinds of routers: small for homes, routers that connect different ISPs or ISPs to enterprises (edge)

## Slide 26: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Processes packets on their way in
Processes packets before they leave
Transfers packets from input to output ports
Input and Output for the same port are on one physical linecard

## Slide 27: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
(1) Implement IGP and BGP protocols; compute routing tables
(2) Push forwarding tables to the line cards

## Slide 28: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)
Constitutes the data plane
Constitutes the control plane
Notes: Control plane: software. Makes decisions over long time horizons.
Data plane: mostly hardware. A decision for each packet.

## Slide 29: Input Linecards: Tasks
Receive incoming packets (physical layer stuff)
Update the IP header (which fields?)
  TTL, Checksum, Options (maybe), Fragment (maybe)
Lookup the output port for the destination IP address
Queue the packet at the switch fabric
Version
Header
Length
Type of Service
(TOS)
Total Length (Bytes)
16-bit Identification
Flags
Fragment Offset
Time to
Live (TTL)
Protocol
Header Checksum
Source IP Address
Destination IP Address
Options (if any)
Payload
Notes: Next: one particular part of the functionality: how to determine the output port for the destination IP address

## Slide 30: Challenge: speed!
100B packets @ 40Gbps  packet every 20 nano secs!
Typically implemented with specialized hardware
  ASICs, specialized “network processors” (return to later)
  “Exception” processing often done at control processor

## Slide 31: Forwarding Table Plays Crucial Role
Table maps IP addresses into output interfaces
Forwards packets based on destination address
…
…
3
1.2.3.6
1
1.2.3.5
1
2
1.2.3.5
1.2.3.4
1.2.3.4
2

## Slide 32: Looking up the output port
Upon receiving a packet
  Inspect the destination IP address in the header
  Index into the forwarding table
  If no match, select the default route
  Forward packet out appropriate interface
Default route
  Configured to cover cases where no matches
  Allows small tables at edge (w/o routing algorithms)
    if it isn’t on my subnet, send it to my ISP

## Slide 33: Scaling the Lookup
One entry for each address  4 billion entries!
For scalability, addresses must be aggregated
But CIDR aggregation makes lookup harder
Notes: How does a router determine which output port for the packet!

## Slide 34: Questions?

## Slide 35: Efficient Packet Lookup

## Slide 36: Lookup with Original or Classful
Early bits in address specify mask
  Class A [0]: /8 (or all addresses in original addressing)
  Class B [10]: /16
  Class C [110]: /24
Can find exact match in forwarding table
  Use prefix as index into hash table
  Each prefix is in one and only one routing entry
This is easy and fast
  Single hash lookup

## Slide 37: Why won’t this work for CIDR?
What’s the network prefix in this address?
11001001 10001111 00000101 11010010
In CIDR, packet can’t tell you network address
  So how do you know which routing entry to use?

## Slide 38: Example #1: Provider w/ 4 Customers
Prefix | Port
201.143.0.0/22 | Port 1
201.143.4.0.0/24 | Port 2
201.143.5.0.0/24 | Port 3
201.143.6.0/23 | Port 4
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Provider
Port 1
Port 2
Port 3
Port 4

## Slide 39: Finding the Match (at ISP’s Router)
No address matches more than one prefix
  But can’t easily find match
Consider 11001001 10001111 0000010111010010
  First 21 bits match 4 partial prefixes
  First 22 bits match 3 partial prefixes
  First 23 bits match 2 partial prefixes
  First 24 bits match exactly one full prefix
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23

## Slide 40: Finding Match Efficiently
Testing each entry to find a match scales poorly
  Roughly (number of entries) × (number of bits)
Must leverage tree structure of binary strings
  Set up tree-like data structure
Return to example:
Prefix | Port
1100100110001111000000********** | 1
110010011000111100000100******** | 2
110010011000111100000101******** | 3
11001001100011110000011********* | 4
Prefix | Port
1100100110001111000000********** | 1
110010011000111100000100******** | 2
110010011000111100000101******** | 3
11001001100011110000011********* | 4

## Slide 41: Consider four three-bit prefixes
Just focusing on the bits where all the action is….
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4

## Slide 42: Tree Structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
Notes: Many more advanced techniques for this….

## Slide 43: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Many more advanced techniques for this….

## Slide 44: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P3
P4
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Many more advanced techniques for this….

## Slide 45: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P3
P4
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Example: 010  P1
Example: 110  P4
Example: 100  P2
Example: 101  P3
walking trees takes O(#bits)
Notes: Many more advanced techniques for this….

## Slide 46: Questions?

## Slide 47: This Example is Too Simple
The prefixes don’t overlap…
...and go to different destinations
  This limits the degree of aggregation
The goal is smaller routing tables
But if the prefixes don’t overlap, we may need to list many prefixes in order to specify all routers
What if 11111111111111111111111111111111 went to port 2, and all other addresses went to port 1?
  How many prefixes would we need in routing table?

## Slide 48: Many Routing Entries…
11111111111111111111111111111111  port 2
11111111111111111111111111111110  port 1
1111111111111111111111111111110/31 port 1
111111111111111111111111111110/30  port 1
11111111111111111111111111110/29  port 1
1111111111111111111111111110/28  port 1
…..

## Slide 49: Avoiding Overlaps is Wasteful
But with overlaps come contradictions….
Remember our old multihoming example?

## Slide 50: Return to Multihoming Global Picture
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
(2) What if we have contradictory entries in routing table?

## Slide 51: We have now returned to problem…
Packets in 201.10.6/23 match two conflicting entries!
  Every address in 201.10.6/23 is also in 201.10.0/21
Which do we take?
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..

## Slide 52: Two ways to write the routing table
Compact but contradictory:
Nonoverlapping (and clear) but verbose:
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 1
201.10.5/24Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
Notes: 201.143.4.0.0/24
201.143.5.0.0/24
201.143.6.0/23

## Slide 53: Change old tree-walking example…
From case where prefixes go to different locations
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4

## Slide 54: …to this
Several of the unique prefixes go to same port
0**  Port 1
100  Port 2
101  Port 1
11*  Port 1
How can we represent this more compactly?

## Slide 55: Prefix Tree
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P1
P1
0**  Port 1
100  Port 2
101  Port 1
11*  Port 1
Notes: Many more advanced techniques for this….

## Slide 56: More Compact Representation
10*
100
0
1**
0
***
1
P2
P1
Record port associated with first match, and only over-ride when it matches another prefix during walk down tree
This is longest prefix match (LPM)
If you ever leave path, you are done, last matched prefix is answer
Notes: Many more advanced techniques for this….

## Slide 57: Longest Prefix Match
***  Port 1
100  Port 2
If address matches both, then take longest match

## Slide 58: Longest Prefix Match Representation
201.143.0.0/21  Port 1
201.143.4.0/24  Port 2
If address matches both, then take longest match
If address matches neither, take default path

## Slide 59: We Use LPM Every Day…..
“Everyone go outside to play….
…except for John, who has to stay inside…”
We routinely insert an “except” whenever we make a general statement and then a contradictory specific statement
Point: we would never explicitly list the members of the class, but instead use the term for the aggregate and then specify the exceptions

## Slide 60: Questions?

## Slide 61: Example #2: Aggregating Customers
Prefix | Port
201.143.0/21 | Provider 1
201.144.0/21 | Provider 2
201.144.0.0/21
201.144.0.0/22
201.144.4.0/24
201.144.5.0/24
201.144.6.0/23
Provider 2
201.143.0.0/21
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Provider 1

## Slide 62: Global Picture
201.143.0/21Port 1
201.144.0/21Port 2
201.145.0/21Port 3
……………..
201.143.0/22Port 1
201.143.4/24Port 2
201.143.5/24Port 3
201.143.6/23Port 4
Router in Internet Core
Router in ISP1
Router in ISP2
201.144.0/22Port 1
201.144.4/24Port 2
201.144.5/24Port 3
201.144.6/23Port 4

## Slide 63: Example #3: Complications
201.144.0.0/21
201.144.0.0/22
201.144.4.0/24
201.144.5.0/24
201.144.6.0/23
Provider 2
201.143.0.0/21
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Provider 1
Forwarding table more complicated when addressing is non-topological
Notes: What does core router do now?

## Slide 64: With nonoverlapping entries..
201.143.0/22Port 1
201.143.4/24Port 1
201.144.4/24Port 1
201.143.6/23Port 1
201.144.0/22Port 2
201.144.5/24Port 2
201.143.5/24Port 2
201.144.6/23Port 2
……………..
201.143.0/22Port 1
201.143.4/24Port 2
201.144.4/24Port 3
201.143.6/23Port 4
Router in Internet Core
Router in ISP1
Router in ISP2
201.144.0/22Port 1
201.144.5/24Port 2
201.143.5/24Port 3
201.144.6/23Port 4

## Slide 65: Matching disjoint prefixes
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
11001001
10010000
000000−−
−−−−−−−
11001001
10010000
00000100
−−−−−−−
11001001
10010000
00000101
−−−−−−−
11001001
10010000
0000011−
−−−−−−−
If match any of these prefixes, go to Provider 1
If match any of these prefixes, go to Provider 2
Notes: No address will match more than one of these prefixes

## Slide 66: Focusing Only on Crucial Bits
1
0
1
0
1
0
1
Prefix destined for Provider 1
Prefix destined for Provider 2
No packet will match more than one prefix
All paths reach a unique prefix
Notes: Many more advanced techniques for this….

## Slide 67: More Compact Representation
0
Prefix destined for Provider 1
Prefix destined for Provider 2
Notes: Many more advanced techniques for this….

## Slide 68: Longest Prefix Match
11001001
10001111
00000−−−
−−−−−−−
Provider 1
201.143.0.0/21
Arriving packet: 11001001 10010000 00000101 01101101
New Arriving packet:
11001001 10010000 00000100 01101101
11001001
10001111
00000101
−−−−−−−
11001001
10010000
00000−−−
−−−−−−−
11001001
10010000
00000100
−−−−−−−
Provider 2
201.144.0.0/21
201.144.4.0/24
201.143.5.0/24

## Slide 69: Return to multihoming example
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 70: Global Picture with Multihoming
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
Which ISP does core send 201.10.6/23 to?
LPM says ISP2…..
Need explicit decisions about prefix granularity
ISP1 might also advertise specific prefix

## Slide 71: LPM in real routers
Real routers use far more advanced/complex solutions than the approaches I just described
  But what we discussed is their starting point
With many heuristics and optimizations that leverage real-world patterns
  Some destinations more popular than others
  Some ports lead to more destinations
  Typical prefix granularities

## Slide 72: Forwarding Summary
Nontrivial to find matches in CIDR
  Because can’t tell where network address ends
  Must walk down bit-by-bit
LPM decreases size of routing table
  Reducing memory consumption

## Slide 73: Questions?

## Slide 74: Conceptual Problems with IP Addressing

## Slide 75: What’s Wrong with IP Addressing?
Multihoming not naturally supported
  Causes aggregation problems
Aggregation relies on addresses being contiguous
  Can’t always apply it where needed
Forwarding hard
  LPM is much harder than exact match
No binding to identity (spoofing, etc.) [discuss later]
Scarce (IPv6 solves this)

## Slide 76: How Can We Avoid These Problems
Problems to be solved:
  Make aggregation more natural
  Accommodate multihoming
  Avoid LPM (use exact match)
Recall our earlier proposal for addressing:
  Rather than stick to 32 bits
  Introduce hierarchical addressing
  Network:Host (or N:H)
  Or M:N:H meaning route to M, then route to N (which lies within M), then to host (which lies in N)

## Slide 77: Advantages
Multihoming natural: host is both N1:H and N2:H
Aggregation is explicit
  If you want to aggregate N1, N2 into M use
    M:N1 and M:N2 as addresses
Routing is exact match (much easier) on M
  And when there is a stack of network addresses…
  Use “deepest match” not longest match
  And this is merely optimization, not correctness issue

## Slide 78: Why Explicit Aggregation?
Can aggregate any two network addresses
  Rule: to use M:N, then M must know how to route to N
No need for numbering and topology to be tied
  Network numbers can have cryptographic significance
Hierarchy of net addresses can use “next header”
  So header remains fixed length….

## Slide 79: Lessons
Think about your goals (aggregation, multihoming,..)
Embed them into the design explicitly
Short term hacks that are implicit in current design will, in the long term, come back to bite you
This has proven true for:
  Aggregation (which uses IP contiguity rather than explicitly stating aggregation)
  Interdomain routing (which reuses IP addressing when one should address domains explicitly)
These mistakes have been very harmful….

## Slide 80: Have a good weekend….