## Slide 1: CS 168 Transport and TCP
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Midterm
No comments until everyone has taken it and final grades are released…
No midterm questions in today’s office hours!
But I do have one announcement…

## Slide 4: You are all seriously fucked for the final..

## Slide 5: Of Pipes, Ports, and Sockets

## Slide 6: Recall Our Last Real Lecture
Transport protocols offer a “pipe” abstraction to applications
Data goes in one end of pipe, emerges at other
Pipes are between processes, not hosts!
There are two basic pipe abstractions….

## Slide 7: Two Pipe Abstractions
Individual message delivery (UDP)
  Unreliable (application responsible for resending)
  Messages limited to single packet
Reliable bytestream delivery (TCP)
  Bytes inserted into pipe by sender
  They emerge, in order, at receiver (to the app)
What features must transport protocols implement to support these abstractions?

## Slide 8: UDP: Datagram messaging service
Multiplexing/Demultiplexing among processes
Discarding corrupted packets (optional)
Nothing else!
A minimal extension of IP

## Slide 9: TCP: Reliable, in-order delivery
Multiplexing/Demultiplexing among processes
Discarding corrupted packets (why not optional?)
Retransmission of lost and corrupted packets
Flow control (to not overflow receiver)
Congestion control (to not overload network)
“Connection” set-up & tear-down

## Slide 10: Connections (or sessions)
Reliability requires keeping state
  Sender: packets sent but not ACKed, and related timers
  Receiver: noncontiguous packets
Each bytestream is called a connection or session
  Each with their own connection state
  State is in hosts, not network!
Example: I am using HTTP to access content on two different hosts, and I’m also ssh’ing into another host. How many sessions is this?

## Slide 11: Services not available
Delay and/or bandwidth guarantees
  This cannot be offered by transport
  Requires support at IP level (and let’s not go there)
Sessions that survive change-of-IP-address
  This is an artifact of current implementations
  As we shall see….

## Slide 12: Ports
Separate 16-bit port address space for UDP, TCP
“Well known” ports (0-1023)
  Agreement on which services run on these ports
  e.g., ssh:22, http:80
  Client (app) knows appropriate port on server
  Services can listen on well-known port
Ephemeral ports (most 1024-65535):
  Given to clients (at random)

## Slide 13: Multiplexing and Demultiplexing
Host receives IP datagrams
  Each datagram has source and destination IP address,
  Each segment has source and destination port number
Host uses IP addresses and port numbers to direct the segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields

## Slide 14
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 15
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload

## Slide 16
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
6 = TCP 17 = UDP
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload

## Slide 17
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
6 = TCP 17 = UDP
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload
16-bit Source Port
16-bit Destination Port
More transport header fields ….

## Slide 18: Connection Mappings
For UDP ports (SOCK_DGRAM)
  OS stores (local port, local IP address)  socket
For TCP ports (SOCK_STREAM)
  (local port, local IP, remote port, remote IP)  socket
Why the difference?
Implications for mobility
Why do you need to include local IP?

## Slide 19: Any Questions?

## Slide 20: UDP

## Slide 21: UDP: User Datagram Protocol
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
  Send messages to and receive them from a socket
UDP described in RFC 768 – (1980)
  IP plus port numbers to support (de)multiplexing
  Optional error checking on the packet contents
    (checksum field = 0 means “don’t verify checksum”)
SRC port
DST port
checksum
length
DATA

## Slide 22: Question
Why do UDP packets carry the sender’s port?

## Slide 23: Why Would Anyone Use UDP?
Finer control over what data is sent and when
  As soon as an application process writes into the socket
  … UDP will package the data and send the packet
No delay for connection establishment
  UDP just blasts away without any formal preliminaries
  … which avoids introducing any unnecessary delays
No connection state
  No allocation of buffers, sequence #s, timers …
  … making it easier to handle many active clients at once
Small packet header overhead
  UDP header is only 8 bytes

## Slide 24: Popular Applications That Use UDP
Some interactive streaming apps
  Retransmitting lost/corrupted packets often pointless - by the time the packet is retransmitted, it’s too late
  E.g., telephone calls, video conferencing, gaming
  Modern streaming protocols using TCP (and HTTP)
Simple query protocols like Domain Name System
  Connection establishment overhead would double cost
  Easier to have application retransmit if needed
“Address for bbc.co.uk?”
“212.58.224.131”

## Slide 25: TCP
We have discussed the general nature of reliable transport. We now focus on it is implemented today.

## Slide 26: Transmission Control Protocol (TCP)
Reliable, in-order delivery (previously, but quick review)
  Ensures byte stream (eventually) arrives intact
    In the presence of corruption and loss
Connection oriented (this lecture)
  Explicit set-up and tear-down of TCP session
Full duplex stream-of-bytes service (this lecture)
  Sends and receives a stream of bytes, not messages
Flow control (this lecture)
  Ensures that sender doesn’t overwhelm receiver
Congestion control (later in semester)
  Dynamic adaptation to network path’s capacity

## Slide 27: Major Notation Change
Previously we focused on packets:
  Packets had numbers
  ACKs referred to those numbers
  Window sizes expressed in terms of # of packets
TCP focuses on bytes. Thus,
  Packets identified by the bytes they carry
  ACKs refer to the bytes received
  Window size expressed in terms of # of bytes
In tests, we will make clear which we mean! But be prepared to use either…..

## Slide 28: Basic Components of Reliability
ACKs
  TCP uses byte sequence numbers to identify payloads
Checksums (to detect corruption)
  TCP checksum over pseudoheader and TCP hdr/payload
Timeouts and retransmissions
  Can’t be reliable without retransmitting lost/corrupted data
  TCP retransmits based on timeouts and duplicate ACKs
  Timeout based on estimate of RTT

## Slide 29: Other TCP Design Decisions
Sliding window flow control
  Allow W contiguous bytes to be in flight
Cumulative acknowledgements
  Selective ACKs (full information) also supported (ignore)
Single timer set after each payload is ACKed
  Timer is effectively for the “next expected payload”
  When timer goes off, resend that payload and wait
    And double timeout period
Various tricks related to “fast retransmit”
  Using duplicate ACKs to trigger retransmission
  Expand window optimistically…

## Slide 30: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 31: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
These should
be familiar

## Slide 32: Segments and Sequence Numbers

## Slide 33: TCP “Stream of Bytes” Service…
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Application @ Host A
Application @ Host B
Byte 80
Byte 80

## Slide 34: … Provided Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out

## Slide 35: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes with Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header  20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
  MSS = MTU – (IP header) – (TCP header)
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 36: Sequence Numbers
Host A
ISN (initial sequence number)
Sequence number = 1st byte in segment = ISN + k
k bytes

## Slide 37: Sequence Numbers
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ACK sequence number
= next expected byte
= seqno + length(data)
Host A
ISN (initial sequence number)
Sequence number = 1st byte in segment = ISN + k
k

## Slide 38: ACKing and Sequence Numbers
Sender sends packet
  Data starts with sequence number X
  Packet contains B bytes
    X, X+1, X+2, ….X+B-1
Upon receipt of packet, receiver sends an ACK
  If all data prior to X already received:
    ACK acknowledges X+B (because that is next expected byte)
  If highest contiguous byte received is smaller value Y
    ACK acknowledges Y+1
    Even if this has been ACKed before

## Slide 39: Pattern (w/ only one packet in flight)
Sender: seqno=X, length=B
Receiver: ACK=X+B
Sender: seqno=X+B, length=B
Receiver: ACK=X+2B
Sender: seqno=X+2B, length=B
Seqno of next packet is same as last ACK field

## Slide 40: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Starting byte offset of data
carried in this segment
Notes: Number of first byte

## Slide 41: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Acknowledgment gives seqno just beyond highest seqno received in order
(“What Byte is Next”)

## Slide 42: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 43: Sliding Window Flow Control
Advertised Window: W
  Can send W bytes beyond the next expected byte
Receiver uses W to prevent sender from overflowing buffer
Limits number of bytes sender can have in flight

## Slide 44: Filling the Pipe
Simple example:
  W (in bytes), which we assume is constant
  RTT (in sec), which we assume is constant
  B (in bytes/sec)
How fast will data be transferred?
If W/RTT < B, the transfer has speed W/RTT
If W/RTT > B, the transfer has speed B

## Slide 45: Advertised Window Limits Rate
Sender can send no faster than W/RTT bytes/sec
In original TCP design, that was the sole protocol mechanism controlling sender’s rate
What’s missing?
Congestion control is about how to adjust W to avoid network congestion (later in semester)
Notes: Being fair to others

## Slide 46: Any Questions?

## Slide 47: Implementing Sliding Window
Sender maintains a window
  Data that has been sent but not yet ACK’ed
Left edge of window:
  Beginning of unacknowledged data
  Moves when data is ACKed
Window size = maximum amount of data in flight
Receiver sets this amount, based on its available buffer space.
  If it has not yet sent data up to app, this might be small
Notes: Picture on board

## Slide 48: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 49: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
“Must Be Zero” 6 bits reserved
Number of 4-byte words in TCP header; 5 = no options

## Slide 50: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Used with URG flag to indicate urgent data (not discussed further)

## Slide 51: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 52: TCP Connection Establishment and Initial Sequence Numbers

## Slide 53: Initial Sequence Number (ISN)
Sequence number for the very first byte
  E.g., Why not just use ISN = 0?
Practical issue
  IP addresses and port #s uniquely identify a connection
  Eventually, though, these port #s do get used again
  … small chance an old packet is still in flight
TCP therefore requires changing ISN
  Set from 32-bit clock that ticks every 4 microseconds
  … only wraps around once every 4.55 hours
To establish a connection, hosts exchange ISNs
  How does this help?

## Slide 54: Establishing a TCP Connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
A
B
Data
Data
Each host tells its ISN to the other host.

## Slide 55: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
ACK
FIN
RST
PSH
URG
See /usr/include/netinet/tcp.h on Unix Systems

## Slide 56: Step 1: A’s Initial SYN Packet
A’s port
B’s port
A’s Initial Sequence Number
(Irrelevant since ACK not set)
Advertised window
5=20B
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
A tells B it wants to open a connection…

## Slide 57: Step 2: B’s SYN-ACK Packet
B’s port
A’s port
B’s Initial Sequence Number
ACK = A’s ISN plus 1
Advertised window
20B
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data
Flags

## Slide 58: Step 3: A’s ACK of the SYN-ACK
A’s port
B’s port
B’s ISN plus 1
Advertised window
20B
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
A tells B it’s likewise okay to start sending
A’s Initial Sequence Number
… upon receiving this packet, B can start sending data

## Slide 59: Timing Diagram: 3-Way Handshaking
Client (initiator)
Server
SYN, SeqNum = x
SYN + ACK, SeqNum = y, Ack = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
connect()
listen()
accept()

## Slide 60: Note: TCP is Duplex
A TCP connection between A and B can carry data in both directions
Packets can both carry data and ACK data
If the ACK flag is set, then it is ACKing data
(details to follow….)

## Slide 61: What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet is lost inside the network, or:
  Server discards the packet (e.g., listen queue is full)
Eventually, no SYN-ACK arrives
  Sender sets a timer and waits for the SYN-ACK
  … and retransmits the SYN if needed
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Hard to guess a reasonable length of time to wait
  SHOULD (RFCs 1122 & 2988) use default of 3 seconds
    Other implementations instead use 6 seconds

## Slide 62: SYN Loss and Web Downloads
User clicks on a hypertext link
  Browser creates a socket and does a “connect”
  The “connect” triggers the OS to transmit a SYN
If the SYN is lost…
  3-6 seconds of delay: can be very long
  User may become impatient
  … and click the hyperlink again, or click “reload”
User triggers an “abort” of the “connect”
  Browser creates a new socket and another “connect”
  Essentially, forces a faster send of a new SYN packet!
  Sometimes very effective, and the page comes quickly

## Slide 63: Tearing Down the Connection

## Slide 64: Normal Termination, One Side At A Time
Finish (FIN) to close connections
  FIN occupies one byte in the sequence space
Other host ack’s the byte to confirm
Closes A’s side of the connection, but not B’s
  Until B likewise sends a FIN
  Which A then acks
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK
Timeout:
Avoid reincarnation
B will retransmit FIN if ACK is lost
Connection now half-closed
Connection now closed
Notes: Why timer? Will get packet with no state!!

## Slide 65: Normal Termination, Both Together
Same as before, but B sets FIN with their ack of A’s FIN
SYN
SYN ACK
ACK
Data
FIN
FIN + ACK
ACK
time
A
B
ACK
Connection now closed
Timeout:
Avoid reincarnation
Can retransmit FIN ACK if ACK lost

## Slide 66: Abrupt Termination
A sends a RESET (RST) to B
  E.g., because app. process on A crashed
That’s it
  B does not ack the RST
  Thus, RST is not delivered reliably
  And: any data in flight is lost
  But: if B sends anything more, will elicit another RST
SYN
SYN ACK
ACK
Data
RST
ACK
time
A
B
Data
RST

## Slide 67: TCP State Transitions
Data, ACK exchanges are in here

## Slide 68: An Simpler View of the Client Side
CLOSED
TIME_WAIT
FIN_WAIT2
FIN_WAIT1
ESTABLISHED
SYN_SENT
SYN (Send)
Rcv. SYN+ACK, Send ACK
Send FIN
Rcv. ACK, Send Nothing
Rcv. FIN, Send ACK

## Slide 69: TCP Retransmission

## Slide 70: Two Mechanisms for Retransmission
Duplicate ACKs
Timeouts

## Slide 71: Loss with cumulative ACKs
Sender sends packets with 100B and seqnos.:
  100, 200, 300, 400, 500, 600, 700, 800, 900
Assume 5th packet (seqno 500) is lost, but no others
Stream of ACKs will be:
  200, 300, 400, 500, 500, 500, 500, 500

## Slide 72: Loss with cumulative ACKs
“Duplicate ACKs” are a sign of an isolated loss
  The lack of ACK progress means 500 hasn’t been delivered
  Stream of ACKs means some packets are being delivered
Therefore, could trigger resend upon receiving k duplicate ACKs
  TCP uses k=3
We will revisit this in congestion control

## Slide 73: Timeouts and Retransmissions
Reliability requires retransmitting lost data
Involves setting timers and retransmitting on timeouts
TCP only has a single timer
TCP resets timer whenever new data is ACKed
Retx packet containing “next byte” when timer expires
RTO (Retransmit Time Out) is basic timeout value

## Slide 74: Setting the Timeout Value (RTO)
1
1
Timeout too long  inefficient
1
1
Timeout too short 
duplicate packets
RTT
Timeout
Timeout
RTT

## Slide 75: Could Base RTO on RTT Estimation
Use exponential averaging of RTT samples
EstimatedRTT
Time
SampleRTT

## Slide 76: Exponential Averaging Example
RTT
time
EstimatedRTT = α*EstimatedRTT + (1 – α)*SampleRTT
Assume RTT is constant  SampleRTT = RTT
0
1
2
3
4
5
6
7
8
9
EstimatedRTT (α = 0.8)
EstimatedRTT (α = 0.5)

## Slide 77: Exponential Averaging in Action
from Jacobson and Karels, SIGCOMM 1988
Set Timeout estimate (ETO) = 2 × EstimatedRTT

## Slide 78: Jacobson/Karels Algorithm
Problem: need to better capture variability in RTT
  Directly measure deviation
Deviation = | SampleRTT – EstimatedRTT |
EstimatedDeviation: exponential average of Deviation
ETO = EstimatedRTT + 4 x EstimatedDeviation

## Slide 79: With Jacobson/Karels

## Slide 80: Problem: Ambiguous Measurements
How do we differentiate between the real ACK, and ACK of the retransmitted packet?
ACK
Retransmission
Original Transmission
SampleRTT
Sender
Receiver
ACK
Retransmission
Original Transmission
SampleRTT
Sender
Receiver

## Slide 81: The Following TCP Rules….
Do not describe current implementations….
...but will be considered the “Truth” in this class

## Slide 82: TCP Timers
Two important quantities:
  RTO: value you set timer to for timeouts
  ETO: current estimate of appropriate “raw” timeout
Use exponential averaging to estimate:
  RTT
  Deviation = | EstimatedRTT – SampleRTT|
ETO = EstimatedRTT + 4 x EstimatedDeviation

## Slide 83: Use Only “Clean” Samples for ETO
Only update ETO when you get a clean sample
Where clean means ACK includes no retransmitted segments

## Slide 84: Example
Send 100, 200, 300
  100 means packet whose first byte is 100, last byte is 199
Receive A200:
  A200 means bytes up to 199 rec’d, expecting 200 next.
  Clean sample
200 times out, resend 200, receive A300
  No clean samples
Send 400, 500, receive A600
  Clean samples

## Slide 85: Setting RTO
Every time RTO timer expires, set RTO  2·RTO
  (Up to maximum  60 sec)
Every time clean sample arrives set RTO to ETO

## Slide 86: Example
First arriving ACK expects 100 (adv. window=500)
  Initialize ETO; RTO = ETO
  Restart timer for RTO seconds (new data ACKed)
    Remember, TCP only has one timer, not timer per packet
  Send packets 100, 200, 300, 400, 500
Arriving ACK expects 300 (A300)
  Update ETO; RTO = ETO
  Restart timer for RTO seconds (new data ACKed)
  Send packets 600, 700
Arriving ACK expects 300 (A300)

## Slide 87: Example (Cont’d)
Timer goes off
  RTO = 2*RTO (back off the timer)
  Restart timer for RTO seconds (it had expired!)
  Resend packet 300
Arriving ACK expects 800
  Don't update ETO (ACK includes a retransmission)
  Restart timer for RTO seconds (new data ACKed)
  Send packets 800, 900, 1000, 1100, 1200

## Slide 88: Example (Cont’d)
Arriving ACK expects 1000
  Update ETO; RTO = ETO
  Restart timer for RTO seconds (new data ACKed)
  Send packets 1300, 1400
… Connection continues …

## Slide 89: This is all very interesting, but…..
Implementations often use a coarse-grained timer
  500 msec is typical
So what?
  Above algorithms are largely irrelevant
  Incurring a timeout is expensive
So we rely on duplicate ACKs

## Slide 90: Any Questions?