## Slide 1: CS 168 How the Internet Works
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Administrivia
Discussion sections start tomorrow
First project out: Aisha Mushtaq lead TA
  You have two weeks from Monday.
Next lecture: layering, principles, history…
  Best lecture of the semester!
Next week: routing!

## Slide 4: Today’s Lecture
Overview of how the Internet works
  Some fundamental concepts: control/data, network stack
  Some fundamental challenges
  General context
Why packets? A fundamental design choice
Packet dynamics
  Delays, queues, and all that….

## Slide 5: Networks Deliver Packets
end-system
switch
link
packet
path

## Slide 6: The Core Task of Internet
Delivers packets between processes (applications) on different hosts (i.e., IPC)
  This involves both the network and network stack
Network: Routers/switches and links
Network stack: networking SW on host
  Stack replicates some router/switch functionality
  Then adds some additional networking functionality…
  ...before handing body of packet to application
  Will discuss this in next lecture

## Slide 7: Packets
Packets are bags of bits with:
  Header: meaningful to network (and network stack)
    Can be more than one protocol header!
  Body: meaningful only to application
Body can be bits in a file, image, whatever
  Can have its own application “header”
What information goes in a header?
Header
Body
Used By Network
and Network Stack
Used By App

## Slide 8: Packets Must Be Sent Along Path
end-system
switch
link
packet
path

## Slide 9: What Must Header Contain For This?
Packet must describe where it should be sent
Requires an address for the destination host
That’s the only way a router/switch can know what to do with the packet

## Slide 10: Names vs Addresses
Network address: where host is located
Network name: which host it is
When you move server to new building
  Name doesn’t change
  But address does change
Same thing with your own name and address!
Let’s get back to packet delivery….

## Slide 11: Packets Must Be Sent Along Path
end-system
switch
link
packet
path

## Slide 12: Fundamental Challenge #1
Route packets through network to destination
Given destination address, how does each switch/router forward packets so that packet reaches destination?
When a packet arrives at a router, the routing table determines which outgoing link the packet is sent on
  Outgoing link is often referred to as a port
  The word port has two meanings in this lecture (later)

## Slide 13: Routing Protocols (Conceptually)
Distributed algorithm run between routers
Gather information about the network topology
Compute paths through that topology
Store forwarding information in each router:
  If packet is destined for X, send out this port
  If packet is destined for Y, send out that port
  …
We call this a routing table

## Slide 14: Control Plane vs Data Plane
Control plane: mechanisms used to compute routing tables (and other forwarding information)
  Inherently global: must know topology to compute
  Routing algorithm is part of the control plane
  Time scale: per network event
Data plane: using those tables to actually forward packets
  Inherently local: depends only on arriving packet and local routing table
  Forwarding mechanism is part of data plane
  Time scale: per packet arrival

## Slide 15: Questions?

## Slide 16: Fundamental Challenge #2
How do you deliver packets reliably?
Packets can be dropped along the way
  Buffers in router can overflow
  Routers can crash while buffering packets
  Links can garble packets
How do you make sure packets arrive safely on an unreliable network?
  Or at least know if they are delivered….
  Want no false positives, and high chance of success

## Slide 17: Two Questions about Reliability
Who is responsible for this? (architecture)
  Network?
  Host?
How is it implemented? (engineering)
We will consider both perspectives….

## Slide 18: Other Important Challenges
Routing with autonomous control
  Internet is comprised of many different ISPs
  More generally called Autonomous Systems (ASes)
  They each get to make their own decisions about how to do routing
  How can you make sure that these independent decisions result in usable end-to-end routes?
Congestion control
  Hosts on the Internet independently decide at what rate they will send packets
  How can you make sure that these independent decisions don’t overload various links?

## Slide 19: What Challenges Have We Missed?
Consider when you access a web page
  Insert URL into browser (e.g., cnn.com)
  Packets sent to web site (reliably)
  Packets reach application on destination host
How do you get to the web site?
  URL is user-level name (e.g., cnn.com)
  Network needs address (e.g., where is cnn.com?)
Must map names to addresses….

## Slide 20: Mapping Names to Addresses
On the Internet, we only name hosts (sort of)
  URLs are based on the name of the host containing the content (i.e., cnn.com names a host)
Before you can send packets to cnn.com, you must resolve names into the host’s address
Done by the Domain Name System (DNS)

## Slide 21: Questions?

## Slide 22: Finishing Our Story
We now have the address of the web site
  So we can send packets to host
  Are we done?
When a packet arrives at a host, what does the host do with it?
  To which process (app) should the packet be sent?
If the packet header only has the destination address, how does the host know where to deliver packet?

## Slide 23: Two Meanings of “Port”
Switches/routers have physical ports:
  Places where links connect to switches
Network stacks have logical ports:
  Logical places where applications connect to stack

## Slide 24: Of Sockets and Ports
When a process wants access to the network, it opens a socket, which is associated with a port
  This is not a physical port, just a logical one
Socket: an OS mechanism that connects processes to the networking stack
Port: number that identifies that particular socket
The port number is used by the OS to direct incoming packets

## Slide 25: Implications for Packet Header
Packet header must include:
  Destination address (used by network)
  Destination port (used by network stack)
When a packet arrives at the destination host, packet is delivered to socket associated with the destination port
Details about sockets in section (tomorrow!)

## Slide 26: Separation of Concerns
Network
  Deliver packets from host to host (based on address)
Network Stack (OS)
  Deliver packets to appropriate socket (based on port)
Applications
  Send and receive packets
  Understand content of packet bodies
Secret of the Internet’s success is getting these and other abstractions right…

## Slide 27: Who Cares?
Why is “separation of concerns” important?
  Separation of Concerns ~ Modularity
Because if each component has a well-defined task, you can focus design on that task
  And replace it with any other implementation that does that task, without changing anything else
When you don’t have separation of concerns, then you have one big pile of code that does everything…
  Very hard to modify, or understand.

## Slide 28: Separation of Concerns
Network
  Deliver packets from host to host (based on address)
Network Stack (OS)
  Deliver packets to appropriate socket (based on port)
Applications
  Send and receive packets
  Understand content of packet bodies

## Slide 29: Review of Important Issues
Routing
Reliable transport
Routing with autonomous control
Congestion control
Mapping names to addresses

## Slide 30: What Else Are We Missing?
How do hosts get their addresses?
  DHCP
What else happens to packets on path?
  Middleboxes
What about security?
  Names play a central role. Why?
What about specialized networks?
  Wireless, Datacenters, Ethernets (L2)
Notes: This completes the list of topics we will cover…

## Slide 31: These Are Our Topics
Each is motivated by a clear problem
The solutions are not always clean or deep
But if you keep in mind what the problem is, you’ll be able to understand the solution

## Slide 32: Questions?

## Slide 33: Why Packets?

## Slide 34: Fundamental Fact About Networks
Must support many “flows” at the same time
Flow = stream of packets sent btwn two hosts
Network must support many simultaneous flows
Which means…

## Slide 35: Links/Switches are Shared
shared link and switch resources

## Slide 36: Two approaches to sharing
Reservations:
  “Flows” reserve bandwidth needed in advance
  Set up circuit and send data over that circuit
    No need for packets
  Must reserve their peak bandwidth
On demand: (also known as “best effort”)
  Break data into packets
  Send packets when you have them
  Hope for the best….

## Slide 37: Example of Statistical Multiplexing
Statistical multiplexing: Combining demands to share resources efficiently
Long history in computer science
  Processes on an OS (vs every process has own core)
  Cloud computing (vs everyone has own datacenter)
Based on the premise that:
  Peak of aggregate load is << aggregate of peak loads
  In fact peak of agg. approaches sum of average loads
Therefore, it is better to share resources than to strictly partition them….

## Slide 38: Two Design Choices
Both embody statistical multiplexing
Reservation: sharing at flow level
  Resources shared between flows currently in system
  Reserve the peak demand for a flow
On-demand: sharing at packet level
  Resources shared between packets currently in system
  Resources given out on packet-by-packet basis
  No reservation of resources

## Slide 39: Two approaches to sharing
Reservations
On demand
How are these implemented?

## Slide 40: Two approaches to sharing
Reservations  circuit switching
  Set up a “circuit”, no need for packets
On demand  packet switching
  Service each packet independently by inspecting its packet header
How are these implemented?

## Slide 41: Circuit Switching
(1) src sends a reservation request for 10Mbps to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 42: Circuit Switching
switch
src
dst
Reservation also establishes a “circuit” within a switch

## Slide 43: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 44: Circuit Switching and Failures
A
B
Circuit switching doesn’t “route around trouble”
Circuit is established
Link Fails along path
Must establish new circuit

## Slide 45: Packet switching
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 46: Packet switching
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 47: Packet Switching and Failures
A
B
Packet switching “routes around trouble”
Link Fails along path
Route recomputed on the fly

## Slide 48: Which is better: Circuits or Packets?
What are the tradeoffs?
Which is better for the Internet?

## Slide 49: Circuits vs Packets
Pros for Circuits:
  Better application performance (reserved bandwidth)
  More predictable and understandable (w/o failures)
Pros for Packets:
  Better efficiency (next slide)
  Simpler state in switches (not per-flow)
  Easier recovery from failure
  Faster startup to first packet delivered

## Slide 50: Example: three constant sources
Total bandwidth 30Mbps
  Mbps = megabits per second
Demands: Each source needs a constant rate of 10Mbps
Reservation and on-demand give same result
  Every source gets what they need
  No wasted bandwidth
  ….

## Slide 51: Example: Three “bursty” sources
12Mbps
Time
Link capacity = 30Mbps
11Mbps
13Mbps

## Slide 52: What happens with reservations?
12Mbps
Option #1: allow two flows to reserve peak rate
Time
Link capacity = 30Mbps
11Mbps
13Mbps
Must turn away third flow!

## Slide 53: What happens with reservations?
12Mbps
Option #2: allow flows to reserve equal rates
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading!

## Slide 54: What happens with on-demand?
No overloading
Time
Link capacity = 30Mbps

## Slide 55: Peak vs Average Rates
For each flow, define:
  P = peak rate
  A = average rate
Reservations must reserve P:
  But flows only use A (on average)
  Level of utilization is A/P
On-demand:
  Can achieve higher utilizations
  Depends on degree of sharing, burstiness of flows
  Peak of aggregate approaches sum of averages

## Slide 56: Smooth vs Bursty Applications
Some apps have relatively small P/A ratios
  Voice might have a ratio of 3:1 or so
Data applications tend to be rather bursty
  Ratios of 100 or greater are common
That’s why the phone network used reservations
  And the Internet does not….

## Slide 57: Questions?

## Slide 58: Packet Delays

## Slide 59: Performance Metrics
Delay
Loss
Throughput

## Slide 60: Delay
How long does it take to send a packet from its source to destination?
Also: How many packets can be “in flight”?
  Already sent, but not yet received

## Slide 61: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 62: Throughput
At what rate is the destination receiving data from the source?

## Slide 63: Today
Focus on delay
Loss and throughput will become relevant in later lectures….

## Slide 64: A network link
Link bandwidth
  Number of bits sent per unit time (bits/sec or bps)
Propagation delay (sometimes called latency)
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time (sent, not recvd)
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 65: Examples of BDP
Same city over a slow link:
  bandwidth: ~100Mbps
  propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Between cities over fast link:
  bandwidth: ~10Gbps
  propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 66: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Processing delay
  Queueing delay
First consider transmission, propagation delays
Then queueing delays
Ignore processing delays (tiny in most cases)
due to link properties
due to traffic mix and
switch internals

## Slide 67: Transmission Delay
Q: How long does it take to push all the bits of a packet into a link?
A: Packet size / Transmission rate of the link
Example: Packet = 1kb, Rate = 100Mbps
  1000 bits / 100 Mbits per sec = 10-5 sec = 10μsec

## Slide 68: Propagation Delay
Q: How long does it take to move one bit from one end of a link to the other?
A: Link length / Propagation speed of link
  Propagation speed ~ some fraction of speed of light
Example: Length = 30 kilometers
  30 kilometers/3x108 meters per sec = 10-4 sec = 100μsec

## Slide 69
transmission
End-to-end delay
propagation
queuing
processing
transmission
propagation
queuing
processing
transmission
propagation

## Slide 70: Now ask a more practical question
Q: How long does it take for a packet to travel from A to B?
A: The delay combines both transmission and propagation delays
  Perhaps also queueing, but ignore those for now

## Slide 71: Example: 100B packet from A to B
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
This is exactly
transmission
plus propogation
delays!

## Slide 72: Example: 100B packet from A to B
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 73: Three cases with 1msec prop. delay
1GB file, 1Gbps link: transmission time dominant
100B packet, 1Gbps link: propagation delay dominant
100B packet, 1Mbps link: transmission ~ propagation
Network design might differ based on which dominates
  But in the Internet, can’t know in advance!

## Slide 74: Technology Trends
Propagation delay?
  No change
Transmission delay?
  Getting smaller!
Queueing delay?
  Usually smaller
How does this affect applications?
  CDNs work very hard to move data near clients
  Reduces backbone bandwidth requirements
  But also decreases latency
  Google: time is money!

## Slide 75: What Trend Did I Leave Out?
The dominance of video
Very high fraction of traffic is video
Files getting larger
But also many, many small flows…
Crucial aspect of Internet traffic:
  Most flows are tiny
  Most bytes in large flows
  Can’t only design for either end of the spectrum

## Slide 76: Queueing and Packet Dynamics

## Slide 77: Queueing Delay

## Slide 78: Queueing Delay
No overload!

## Slide 79: Queueing Delay
Transient Overload
Not a rare event!
Queue

## Slide 80: Queueing Delay
Queue
Transient Overload
Not a rare event!

## Slide 81: Queueing Delay
Queue
Transient Overload
Not a rare event!

## Slide 82: Queueing Delay
Queue
Transient Overload
Not a rare event!

## Slide 83: Queueing Delay
Queue
Transient Overload
Not a rare event!

## Slide 84: Queueing Delay
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts but introduce queueing delay

## Slide 85: Queueing Delay
What about persistent overload?
Will eventually drop packets (“loss”)

## Slide 86: More packet animations….

## Slide 87: The Lifecycle of Packets
Excess Packets
Stored in Buffer
Packet Arriving
at Switch
Packet
Being
Transmitted
Packet Buffer
Link
Packet Currently
Being Transmitted

## Slide 88: The Delays of Their Lives
Queueing
Delay
Transmission
Delay
Propagation Delay is how long it takes
to reach the next switch after transmission
Round-Trip Time (RTT) is the time it takes
a packet to reach the destination and
the response to return to the sender

## Slide 89: Smooth Arrivals = No Queueing Delays

## Slide 90: Bursty Arrivals = Queueing Delays
There is substantial queueing delay even though link is underutilized

## Slide 91: Packet Losses: Buffers Full

## Slide 92: Packet Losses: Corruption

## Slide 93: About Today’s Lecture
The Internet is a huge, complicated system
One can study the parts in isolation
  Routing
  Congestion control
  ….
But the pieces all fit together in a particular way
Today was quick overview of how pieces fit...
  Don’t worry if you didn’t understand much of it
  You probably absorbed more than you realize

## Slide 94: Thursday’s lecture….
Layering, principles, the “good stuff”
Read K&R 1.4-1.8 (mostly for context)