## Slide 1: CS 168 The End of Congestion Control
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Announcements
Participation: (see Piazza post and followup rules)
  293 of you have recorded participation
  234 of you have not!
  There are 6 more classes and 3 more OHs
  I will show no mercy: either participate or fail.
Detailed Example
  Two weeks ago I went through a detailed example
  I have now posted that example
  Please go over it carefully; make sure you understand
  This is fair game for the final….

## Slide 4: The Many Failings of TCP CC
Cumulative ACKs are stupid
Fills up queues (large delays)
Depends on losses (noncongestive losses)
Does not scale to high-speed
Produces irregular saw-tooth behavior
Depends on RTT (unfair)
Takes a long time to reach steady state
Easy to cheat
Relies on homogeneity for performance/fairness

## Slide 5: Purpose of Today
The problems (and solutions) are not main point
  Though you need to know them
But are a way to get you to think more generally
  Beyond congestion control (CC) as a TCP cookbook
Both about CC and other protocol design tasks
(Will skip some sections of lecture as needed)

## Slide 6: Examples of Issues Addressed
How can cheating hurt?
What is fairness?
How does fairness help innovation?
What is the golden rule of research?

## Slide 7: (2) TCP fills up queues
TCP only slows down when queues fill up
Means that delays are large for everyone
And many packets are dropped when buffer fills
  Not always, but it does tend to increase packet drops
Alternative: Random Early Drop (LBL)
  Drop packets on purpose before queue is full
  This was a very clever idea….

## Slide 8: Random Early Drop (or Detection)
Measure avg queue size A with exp. weighting
  Avg: Allows short bursts of packets without over-reacting
Drop probability is a function of A
  No drops if A is very small
  Low drop rate for moderate A’s
  Drop everything if A is too big
Drop probability applied to incoming packets
Intuition: link is fully utilized well before buffer is full

## Slide 9: RED Dropping Probability

## Slide 10: Advantages of RED
Keeps queues smaller, while allowing bursts
  Just using small buffers in routers can’t do the latter
Reduces synchronization between flows
  Not all flows are dropping packets at once
  Increases/decreases are more gentle
Now being used to reduce buffer-bloat
  “buffer-bloat”: experiencing large delays
  Try uploading large file from home…
Notes: …

## Slide 11: Why Isn’t RED Fair?
RED gives all flows roughly the same drop rate
The TCP equation gives the following
Resulting throughputs depend on RTT…
I had a competing proposal called FQ
  More on that later

## Slide 12: History of RED
RED proposed (Floyd and Jacobson)
  Huge support from research community
  Operators find it hard to configure, see few advantages
Adaptive RED (Floyd)
  Self-configuring version of RED. Largely ignored.
CoDel (Nichols and Jacobson)
  Cleaner self-configuring version of RED.
  Lots of press (bufferbloat)
Implementors adopt FQ-CoDel
  Karma’s a bitch!

## Slide 13: (3) Non-congestion-related Losses?
Can use Explicit Congestion Notification (ECN)
Bit in IP packet header (actually two)
  TCP receiver returns this bit in ACK
  Think about this!
When RED router would drop, it sets bit instead
  Congestion semantics of bit exactly like that of drop
Advantages:
  Doesn’t confuse corruption with congestion
  Doesn’t confuse recovery with rate adjustment

## Slide 14: (4) Does AIMD work at high speed?
Throughput = (MSS/RTT) sqrt(3/2p)
  Assume that RTT = 100ms, MSS=1500bytes
What value of p is required to go 100Gbps?
  Roughly 2 x 10-12
How long between drops?
  Roughly 16.6 hours
How much data has been sent in this time?
  Roughly 6 petabits
These are not practical numbers!

## Slide 15: Adapting TCP to High Speed
One approach:
  Let AIMD “constants” depend on CWND
At very high speeds,
  Increase CWND by more than MSS in a RTT
  Decrease CWND by less than ½ after a loss
We will discuss other approaches later…

## Slide 16: High-Speed TCP Proposal (Floyd)
Bandwidth | AvgCwnd (pkts) | Increase a(w) | Decrease b(w)
1.5 Mbps | 12.5 | 1 | 0.50
10 Mbps | 83 | 1 | 0.50
100 Mbps | 833 | 6 | 0.35
1 Gbps | 8333 | 26 | 0.22
10 Gbps | 83333 | 70 | 0.10

## Slide 17: High-Speed TCP

## Slide 18: This changes the TCP Equation
Throughput ~ p-.8 (rather than p-.5)
  Packet drops every tens of seconds
To achieve high throughput:
  Don’t need such a tiny drop rate…
  Can ramp up more quickly
How can this coexist with normal TCP?
  Only invoke new parameters at large window sizes
  Competes fairly with normal TCP at normal speeds

## Slide 19: (5) Sawtooth Behavior Uneven
TCP throughput is “choppy”
  Repeated swings between W/2 to W
Some apps would prefer sending at a steady rate
  e.g., streaming apps
A solution: “Equation-Based Congestion Control”
  Ditch TCP’s increase/decrease rules and just follow the equation
  Measure drop percentage p, and set rate accordingly
Following the TCP equation ensures we’re “TCP friendly”
  i.e., use no more than TCP does in similar setting

## Slide 20: These Problems Are All Solved
With published and often standardized solutions
TCP-SACK
RED (and its many variants)
ECN
High-Speed TCP
Equation-based congestion control (EBCC)
Datagram congestion control protocol (DCCP)
Some widely used, others not….

## Slide 21: Any Questions?

## Slide 22: (6) Bias Against Long RTTs
Flows get throughput inversely proportional to RTT
TCP unfair in the face of heterogeneous RTTs!
A1
A2
B2
B1
bottleneck
link
100ms
200ms

## Slide 23: Possible Solutions?
Make additive constant proportional to RTT
But people don’t really care about this….

## Slide 24: (7) How do short flows fare?
50% of flows have < 1500B to send; 80% < 100KB
Short flows are slowed down by slow-start
  It takes several round-trips to send 8 packets!
    Handshake, CWND=1, CWND=2, CWND=4, CWND=8
Too few packets to trigger dupACKs
  Isolated loss may lead to timeouts
At typical timeout values of ~500ms…
  ...might severely impact flow completion time

## Slide 25: Possible Solutions?
Larger initial window?
  Google proposed moving from ~4KB to ~15KB
  Covers ≈90% of HTTP Web
  Decreases delay by ~5%
Recursively cautious congestion control (RC3)
  Run normal TCP at normal priority
  Send aggressively at lower priorities
  With a limit on each priority level
  Ramps up to full speed immediately, no harm to others
  I failed at providing better QoS; this exploits worse QoS!

## Slide 26: (8) Cheating
TCP was designed assuming a cooperative world
No attempt was made to prevent cheating
Many ways to cheat, will present three

## Slide 27: Cheating #1: ACK-splitting (Rcvr)
Round-
Trip
Time
(RTT)
Sender
Receiver
ACK 486
Data 4381:5841
Data 1461:2921
Data 2921:4381
Data 5841:7301
ACK 973
ACK 1461
Data 1:1461
Rule: grow window by one
full-sized packet for each
valid ACK received
Send M (distinct) ACKs for one packet
Growth factor proportional
to M
What’s the fix?

## Slide 28: 10 line change to Linux TCP
(Courtesy of
Stefan Savage)

## Slide 29: Cheating #2: Increasing CWND Faster
Limit rates:
x = 2y
C
x
y
x increases by 2 per RTT
y increases by 1 per RTT

## Slide 30: Cheating #3: Open Many Connections
A
B
x
D
E
y
Assume
A starts 10 connections to B
D starts 1 connection to E
Each connection gets about the same throughput
Then A gets 10 times more throughput than D

## Slide 31: Cheating
Either sender or receiver can independently cheat!
Why hasn’t Internet suffered congestion collapse yet?
  Individuals don’t hack TCP (not worth it)
  Companies need to avoid TCP wars
How can we prevent cheating?
  Verify TCP implementations?
  Controlling end points is hopeless!
So what should we do?

## Slide 32: (9) Converse of Cheating
To be fair, need to be TCP-friendly
  The requirement that whatever CC you use, it competes fairly with TCP
Everyone uses “similar” CC algorithm
  This doesn’t apply in your own datacenters
  But does apply in Internet more generally
Slows down innovation!

## Slide 33: Any Questions?

## Slide 34: How do you solve these problems?
Bias against long RTTs
Slow to ramp up (for short flows)
Cheating
Need for uniformity

## Slide 35: Get the Network Involved!
How can routers help?
Routers can provide guidance for speed to send at
  Routers have better visibility, and their feedback flows through network, collecting from routers along path
Routers can provide isolation/fairness
  Via packet scheduling
Routers can provide priority for some flows
  Via packet scheduling

## Slide 36: How Does This Help?
Guidance for sending rate deals with
  Slow to ramp up
  Bias against long RTTs
  Does not deal with cheating or need for uniformity
Providing Isolation/Fairness deals with
  Prevents most cheating, allows innovation
  Innovation deals with bias and ramp up
Priorities
  You’ll see….

## Slide 37: Routers tell hosts how fast to send
Packets carry “rate field”
Routers insert “fair share” f in packet header
  Only insert if your f is smaller than current field
  Source then sees minimum fair share along path
End-hosts set sending rate (or window size) to f
This is the basic idea behind the “Rate Control Protocol” (RCP) from Dukkipati et al. ’07

## Slide 38: A Few More Details
How does this work?
  Router estimates rate f that will use its capacity
  Adaptive process of guessing (why not exact?)
    Link underutilized: increase f Link congested: decrease f
Why does this work?
  Flows get immediately up to speed
  And no need to “probe” (gently or otherwise)
TCP still does loss recovery through retx’s
  But does not need to worry about adjusting CWND based on these….

## Slide 39: How This Helps! (Ignore XCP)

## Slide 40: Any Questions?

## Slide 41: How can routers ensure each flow gets its “fair share”?

## Slide 42: Isolation
Treat each “flow” separately
  For now, flows are packets between same Source/Dest.
Each flow has its own FIFO queue in router
Service flows in a round-robin fashion
  When link becomes free, take packet from next flow
Assuming all flows are sending MTU packets, all flows can get their fair share

## Slide 43: Benefits
Each flow can use their own adjustment algorithm
  Perhaps aided by the router telling them how fast to send
If I send too fast, only my packets are dropped
  I can’t hurt other users…
This solves the innovation problem!
  People can experiment with any CC algorithm
And the cheating problem!
  No matter what you do, you can’t get more than your share

## Slide 44: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 45: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 46: Consider a Simple Model
Flows ask for an amount of bandwidth ri
  In reality, this request is implicit (the amount they send)
The link gives them an amount ai
  Again, this is implicit (by how much is forwarded)
  ai ≤ ri
There is some total capacity C
  Sum ai ≤ C

## Slide 47: Fairness
When all flows want the same rate, fair is easy
  Fair share = C/N
  C = capacity of link
  N = number of flows
Note:
  This is fair share per link. This is not a global fair share.
When not all flows have the same demand?
  What happens here?

## Slide 48: Example 1
Requests: ri Allocations: ai
C=20
  Requests: r1=6, r2=5, r3=4
Solution: a1=6, a2=5, a3=4
When bandwidth is plentiful, everyone gets their request
This is the easy case

## Slide 49: Example 2
C=12
  Requests: r1=6, r2=5, r3=4
One solution: a1=4, a2=4, a3=4
  Everyone gets the same
Why not proportional to their demands?
  ai = (12/15)ri
Asking for more gets you more!
  Not incentive compatible (i.e., cheating works)
  You can’t have that and invite innovation!

## Slide 50: Example 3
C=14; Requests: r1=6, r2=5, r3=4
a3=4 (can’t give more than a flow wants)
Remaining bandwidth is 10, with demands 6 and 5
  From previous example, if both want more than their share, they both get half
  a1=a2=5

## Slide 51: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
or set f to be infinite if no such value exists
This is what round-robin service gives
  if all packets are MTUs
Property:
  If you don’t get full demand, no one gets more than you

## Slide 52: Computing Max-Min Fairness
Assume demands are in increasing order….
If C/N ≤ r1, then ai = C/N for all i.
Else, a1 = r1, set C = C-a1 and N = N-1
Repeat
Intuition: all flows requesting less than fair share get their request. Remaining flows divide equally.

## Slide 53: Example
Assume link speed C is 10mbps
Have three flows:
  Flow 1 is sending at a rate 8mbps
  Flow 2 is sending at a rate 6mbps
  Flow 3 is sending at a rate 2mbps
How much bandwidth should each get?
  According to max-min fairness?
Work this out, talk to your neighbors

## Slide 54: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 55: Max-Min Fairness
Max-min fairness the natural per-link fairness
Only one that is:
  Symmetric
  Incentive compatible (asking for more doesn’t help)
Why is incentive compatibility important here, but not for TCP (where we ignore cheating)?
  TCP requires uniformity, FQ enables innovation
  Want to make sure innovation does not hurt others!

## Slide 56: Reality Of Congestion Control
Congestion control is a resource allocation problem involving many flows, many links, and complicated global dynamics
1Gbps
600Mbps
1Gbps

## Slide 57: Network As A Whole….
Is way more complicated! But calculating allocations just a bit more complicated….
Start with switch a with smallest Ca/Na
Apply algorithm to smallest ri at switch
Remove that flow from system, adjusting C and N where appropriate (all hops along path).
Repeat

## Slide 58: Any Questions?

## Slide 59: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 60: Dealing with different packet sizes
Mental model: Bit-by-bit round robin (“fluid flow”)
  Treat every bit as a separate packet!
Can you do this in practice?
No, packets cannot be shredded into separate bits
But we can approximate it
  This is what “fair queuing” routers do

## Slide 61: Fair Queuing (FQ)
For each packet, compute the “round” in which the last bit of a packet would have left the router if flows are served bit-by-bit round-robin
  Ai = arrival time (in rounds) of ith packet in flow
  Pi = size of ith packet in flow
  Si = start time (round) of ith packet in flow
  Fi = finish time (round) of ith packet in flow
  Si = MAX[Ai, Fi-1]
  Fi = Si + Pi
Then serve packets in the increasing order of their finish times Fi

## Slide 62: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Service
in fluid flow
system
FQ Packet
system
time
time
time
time

## Slide 63: Fair Queuing (FQ)
Implementation of round-robin generalized to case where not all packets are MTUs
Weighted fair queueing (WFQ) lets you assign different flows different shares
WFQ is implemented in almost all routers
  Not true in the 1980-90s, when CC was being developed
  Mostly used to isolate larger granularities (e.g., per-prefix)

## Slide 64: FQ vs. FIFO
FQ advantages:
  Cheating flows don’t benefit
  Bandwidth share does not depend on RTT
  Flows can pick any rate adjustment scheme they want
Disadvantages:
  More complex than FIFO: per flow queue/state, additional per-packet book-keeping

## Slide 65: Role in “Control Theory” Literature
When you have FQ routers, the network is globally stable as long as every congestion control algorithm is “unilaterally stable”.
  If each flow is stable (holding others fixed) then system is stable. Why?
This is not true with FIFO routers….
There’s an interesting theory question here:
  What kinds of unilateral stability guarantee global stability with FIFO?
  Conjecture about guaranteed unilateral stability…..
    Haven’t thought about in years, but seems doable

## Slide 66: Role in Economics Literature
FQ became “serial cost sharing”
  Herve’ Moulin: “You are stupid: your mechanism is neat”
Applies to problems where total cost increases with total usage, but agents want different amounts
  Serial cost sharing is strategy-proof, and uniquely so…
  Very strong strategic properties (e.g., coalitions, etc.)
Now a popular cost sharing mechanism in econ
  Not the most “fair” but it is the most “stable”….
  In econ, if allocation isn’t stable, then it isn’t relevant…..

## Slide 67: Line of Networking Research
If you assume all users are selfish, how can you design network so that the resulting outcome is socially optimal?
FQ is the answer for packet scheduling.
But the question is more generally applicable
This is not about celebrating greed, but about how to design complicated distributed systems that can achieve socially optimal outcomes….
  Selfish behavior is merely doing local maximization
  Nice if that results in overall system optimality

## Slide 68: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement FQ?
And what’s wrong with this approach?

## Slide 69: Fairness Through Dropping
Traditional FQ uses scheduling to achieve fairness
  Scheduling: order in which packets are sent
But note that dropping is sufficient to give fairness
Assume a set of incoming rates ri
Dropping at rates pi = MAX[0,1-f/ri] yields fairness
ri(1-pi) = Min[ri,f]

## Slide 70: Contrast with RED
RED: all flows have same drop probability
FQ via dropping: per-flow drop probabilities

## Slide 71: Two Dropping Approaches
Estimate rate ri at edge, stick in packet header
  Then individual routers drop with probability 1-f/ri
  Where each router computes its own f
Estimate rate at every router using “shadow buffer”
  See how many packets of a flow are in shadow buffer
  Use this to estimate ri
  Why does this simple estimation strategy work?
  Implemented on significant fraction of Cisco product line

## Slide 72: Any Questions?

## Slide 73: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 74: flow rate fairness dismantling a religion <draft-briscoe-tsvarea-fair-01.pdf>
Bob Briscoe
Chief Researcher, BT Group
IETF-68 tsvwg Mar 2007

## Slide 75: Giving equal shares to “flows” is silly
What if you have 8 flows, and I have 4…
  Why should you get twice the bandwidth?
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why not penalize for using more scarce bandwidth?
And what is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 76: Charge people for congestion!
Use ECN as congestion markers
Whenever I get ECN bit set, I have to pay $$$
No debate over what a flow is, or what fair is…
Idea started by Frank Kelly, backed by much math
  Great idea: simple, elegant, effective
  Never going to happen…
Cannot bake economics into architecture….

## Slide 77: Review of Network Involvement
We have considered two approaches:
  Providing guidance for sending rate
  Providing isolation/fairness
What have we left out?
  Providing priority for some flows
To motivate this, we need to step back….

## Slide 78: What Is Metric of Success?
You want to improve application performance!
And how do you do that?
By minimizing flow completion time (FCT)
We have said congestion control should utilize available bandwidth, minimize packet delay
  But these are only means to a higher goal
The ultimate goal is minimizing FCT

## Slide 79: Theory Result
At a single router, to minimize FCT you prioritize packets in terms of the shortest remaining processing time (SRPT)
In other words: packets whose flows are closest to finishing are sent first
If you don’t know how many bytes have left, then round-robin (FQ) is best you can do
  FQ FCT much better than FIFO FCT
But if you know, then you can do SRPT directly
  Ignore the issue of how you know

## Slide 80: Example
Flow A of size 15 (packets) arrives first.
Then Flow B of size 2 (packet) arrives, right after first packet of Flow A starts transmission.
  Assume each packet takes one time unit.
FIFO: Average FCT = 16
  Flow A finishes at time 15, Flow B finishes at time 17
FQ: Average FCT = 10.5
  Flow B finishes at time 4, Flow A at time 17
SRPT: Average FCT = 10
  Flow B finishes at time 3, Flow A at time 17

## Slide 81: Practical Result
Once you put SRPT scheduling in router
  Doesn’t matter what endpoints do as long as isn’t stupid
But if you have FIFO, then it matters a lot how you respond to congestion.
DCTCP is a sophisticated CC design
minTCP is a very simple CC design

## Slide 82: Implications for CC Research
Most important task: Make SRPT practical
Router mechanisms….can use regular priority Qs
Host mechanisms to make flow size visible
  Straightforward.....
Highly applicable to datacenters (perf. important)
  Doubtful for wide-area...(where fairness more important)

## Slide 83: History of Congestion Control Rsch
The early days:
  Jacobsen/DEC invented modern CC
  Then many papers on small variations
Continued stream of papers
  Small hacks for how flows should react to congestion
  Control theory
Datacenters!
  Can actually deploy
  Performance extremely critical
  More hacks for how flows should react to congestion

## Slide 84: But if you use SRPT
Then most of the congestion control research on how to respond to congestion is a waste of time…
Golden rule of research:
  If you can’t come up with good ideas on your own
  Then prove that their research is a waste of time...