## Slide 1: CS 168 Software-Defined Networking
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Goal for Today
Provide the “why” of software-defined networking
  Some history
  Some gossip
  And an exercise in retrospective architectural thinking
Not much of the “what”
  Go read papers (NOX, ONIX, NetVirt, Fabric, …)
  Besides, the details are boring….

## Slide 4: Caveats and Context

## Slide 5: Caveats
I cofounded a startup (Nicira) that worked on SDN
  With Martín Casado and Nick McKeown
  My views on SDN may therefore be biased
  I have no financial interest in the outcome, just ego
SDN is not a revolutionary technology…
  …just a way of organizing network functionality
But that’s all the Internet architecture is….
  The Internet architecture isn’t clever, but it is deeply wise
  We know SDN isn’t clever, but we hope it is wise….

## Slide 6: Context
Where did SDN come from?
And what is the state of networking as a field?
Keep context in mind as you learn about SDN…
  It will clarify why we think SDN is a big deal
  And why it took us so long to wake up….

## Slide 7: C#1: Where did SDN come from?
~2004: Research on new management paradigms
  RCP, 4D [Princeton, CMU,….]
  SANE, Ethane [Stanford/Berkeley]
  Industrial efforts with similar flavor (not published)
2008: Software-Defined Networking (SDN)
  NOX Network Operating System [Nicira]
  OpenFlow switch interface [Stanford/Nicira]
2011: Open Networking Foundation (ONF)
  Board: Google,Yahoo,Verizon,DT,Msft, Fbook,NTT,GS
  Members: Cisco, Juniper, HP, Dell, Broadcom, IBM,…..

## Slide 8: Where did SDN really come from?
Martín Casado

## Slide 9: Quote from a Wired profile….
“Martin Casado is fucking amazing,” says Scott Shenker ….. “I’ve known a lot of smart people in my life, and on any dimension you care to mention, he’s off the scale.”

## Slide 10: Current Status of SDN
SDN widely accepted as “future of networking”
  Commercialized, in production use, growing revenue
    E.g., controls Google’s networks, carriers adopting
An insane level of SDN hype, and backlash…
  SDN doesn’t work miracles, merely makes things easier
  The fight isn’t over whether SDN will be adopted, but which version of SDN will be adopted….
But the real question is: why the rapid adoption?
  2004: idea, 2008: design, 2011: industry frenzy
  Many better research ideas have gone nowhere!

## Slide 11: C#2: The Field of Networking…
Research built a great artifact: Internet
  Mostly unrelated to academic research which came later
CS networking now largely the study of the Internet
Also interesting research in wireless, optical
  Much of it is EE research into underlying technologies
  Some wireless research (such at Katabi at MIT) broader
But we failed to create an academic discipline

## Slide 12: Building an Artifact, Not a Discipline
Other fields in “systems”: OS, DB, etc.
  Teach basic principles
  Are easily managed
  Continue to evolve
Networking:
  Teach big bag of protocols
  Notoriously difficult to manage
  Evolves very slowly
Networks are much more primitive and less understood than other computer systems

## Slide 13: We are left with two key questions
Why the rapid adoption of SDN?
  What problem is it solving?
Why is networking behind other fields in CS?
  What is missing in the field?
The answers are related, but will unfold slowly
  Starting with a discussion of Network Management

## Slide 14: Network Management

## Slide 15: What is Network Management?
Recall the two “planes” of networking
Data plane: forwarding packets
  Based on local forwarding state
Control plane: computing that forwarding state
  Involves coordination with rest of system
Broad definition of “network management”:
  Everything having to do with the control plane

## Slide 16: Original goals for the control plane
Basic connectivity: route packets to destination
  Local state computed by routing protocols
  Globally (intradomain) distributed algorithms
Interdomain policy: find policy-compliant paths
  Done by globally (interdomain) distributed BGP
For long time, these were the only relevant goals!
  What other goals are there in running a network, now?

## Slide 17: Isolation
L2 bcast protocols often used for discovery
  Useful, unscalable, invasive
Want multiple logical LANs on a physical network
  Retain usefulness, cope with scaling, provide isolation
Use VLANs (virtual LANs) tags in L2 headers
  Controls where broadcast packets go
  Gives support for logical L2 networks
  Routers connect these logical L2 networks
No universal method for setting VLAN state

## Slide 18: Access Control
Operators want to limit access to various hosts
  “Don’t let laptops access backend database machines”
This can be imposed by routers using ACLs
  ACL: Access Control List
Example entry in ACL: <header template; drop>
  If not port 80, drop
  If source address = X, drop
These are typically configured manually

## Slide 19: Traffic Engineering
Want to avoid persistent overloads on links
Choose routes to spread traffic load across links
Two main methods:
  Setting up MPLS tunnels (MPLS is layer 2.5)
  Adjusting weights in OSPF
Often done with centralized computation
  Take snapshot of topology and load
  Compute appropriate MPLS/OSPF state
  Send to network

## Slide 20: Net management has many goals
Achieving these goals is job of the control plane…
…which currently involves many mechanisms
Globally distributed: routing algorithms
Manual/scripted configuration: ACLs, VLANs
Centralized computation: Traffic engineering

## Slide 21: Bottom Line
Many different control plane mechanisms
Each designed from scratch for their intended goal
Encompassing a wide variety of implementations
  Distributed, manual, centralized,…
And none of them particularly well designed
Network control plane is a complicated mess!

## Slide 22: How Have We Managed To Survive?
Net. admins miraculously master this complexity
  Understand all aspects of networks
  Must keep myriad details in mind
This ability to master complexity is both a blessing
  …and a curse!

## Slide 23: A Simple Story About Complexity...
~1985: Don Norman visits Xerox PARC
  Talks about user interfaces and stick shifts
  Do you even know what a stick shift is?

## Slide 24: What Was His Point?
The ability to master complexity is valuable
  But not the same as the ability to extract simplicity
Each has its role:
  When first getting systems to work, master complexity
    Stick shifts!
  When making system easy to use, extract simplicity
    Automatic transmissions!
You will never succeed in extracting simplicity
  If you don’t recognize it is a different skill set than mastering complexity!

## Slide 25: What Is My Point?
Networking has never made the distinction…
  And therefore has never made the transition from mastering complexity to extracting simplicity
Still focused on mastering complexity
  Networking “experts” are those that know all the details
Extracting simplicity lays intellectual foundations
  By providing elegant conceptual formulations
This is why networking has weak foundation
  We are still building the artifact, not the discipline

## Slide 26: More Progress Recently
There have been attempts to extract simplicity
  Mostly following from SDN
But they are isolated to individual papers
The field as a whole is still far from a conceptually-oriented discipline
Partly because we cannot change current architecture, so we have to teach what is….

## Slide 27: Have answered one of our questions
The reason networking is not a discipline is because it has not sought to extract simplicity
  Other fields, such as OS, DB, etc, have
  Those fields are more mature
One reason for this difference
  They can build their own artifacts, we are tied to Internet
Extracting simplicity is also how you generalize to larger, more complicated systems
  So it has practical advantages as well….

## Slide 28: Forcing people to make the transition
We are really good at mastering complexity
  And it has worked for us for decades, why change?
How do you make people change?
  Make them cry!
A personal story about algebra and complexity
  School problems:
  3x + 2y = 8 x + y = 3
  My father’s problems:
  327x + 26y = 8757 45x + 57y = 7776
Notes: 17, 123

## Slide 29: Making Network Operators Cry…

## Slide 30: Step 1: Large datacenters
100,000s machines; 10,000s switches
This is pushing the limits of what we can handle….

## Slide 31: Step 2: Multiple tenancy
Large datacenters can host many customers
Each customer gets their own logical network
  Customer should be able to set policies on this network
  ACLs, VLANs, etc.
If there are 1000 customers, that adds 3 oom
  Where oom = orders of magnitude
This goes way beyond what we can handle
  Because our control plane is so primitive!

## Slide 32: Net Operators Were Now Weeping…
They had been beaten by complexity
The era of ad hoc control mechanisms was over
We needed a simpler, more systematic design
Which is the answer to: why the rapid adoption?
  Also, everyone hated Cisco….
So we had to “extract simplicity”!
So how do you “extract simplicity”?

## Slide 33: An Example Transition: Programming
Machine languages: no abstractions
  Had to deal with low-level details
  Mastering complexity was crucial
Higher-level languages: OS and other abstractions
  File system, virtual memory, abstract data types, ...
Modern languages: even more abstractions
  Object orientation, garbage collection,...
Abstractions key to extracting simplicity

## Slide 34: “The Power of Abstraction”
“
Modularity based on abstraction
is the way things get done”
−Barbara Liskov
Abstractions  Interfaces  Modularity

## Slide 35: What About Network Abstractions?
Consider the data and control planes separately
Different tasks, so naturally different abstractions

## Slide 36: Abstractions for Data Plane: Layers
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 37: Control Plane Abstractions
?

## Slide 38: Many Control Plane Mechanisms
Variety of goals, no modularity:
  Routing: distributed routing algorithms
  Isolation: ACLs, VLANs, Firewalls,…
  Traffic engineering: adjusting weights, MPLS,…
Control Plane: mechanism without abstraction
  Too many mechanisms, not enough functionality

## Slide 39: Finding Control Plane Abstractions

## Slide 40: How do you find abstractions?
You first decompose the problem….
…and define abstractions for each subproblem
So what is the control plane problem?

## Slide 41: Decomposing the Control Plane
What problem is it solving?
Decompose it like we did the data plane
  i.e., break it down into smaller problems….
Talk to your neighbors.
Don’t look ahead at the slides.
3 minutes

## Slide 42: Task: Compute forwarding state
Consistent with low-level hardware/software
  Which might depend on particular vendor
Based on entire network topology
  Because many control decisions depend on topology
For all routers/switches in network
  Every router/switch needs forwarding state
Notes: Do this in different order!!!

## Slide 43: Our current approach
Design one-off mechanisms that solve all three
A sign of how much we love complexity
No other field would deal with such a problem!
They would define abstractions for each subtask
…and so should we!

## Slide 44: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 45: Abs#1: Forwarding Abstraction
Express intent independent of implementation
  Don’t want to deal with proprietary HW and SW
OpenFlow is current proposal for forwarding
  Standardized interface to switch
  Configuration in terms of flow entries: <header, action>
Design details concern exact nature of:
  Header matching
  Allowed actions

## Slide 46: Two Important Facets to OpenFlow
Switches accept external control messages
  Not closed, proprietary boxes
Standardized flow entry format
  So switches are interchangable

## Slide 47: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 48: Abs#2: Network State Abstraction
Abstract away various distributed mechanisms
Abstraction: global network view
  Annotated network graph provided through an API
Implementation: “Network Operating System”
  Runs on servers in network (“controllers”)
  Replicated for reliability
Information flows both ways
  Information from routers/switches to form “view”
  Configurations to routers/switches to control forwarding

## Slide 49: Network Operating System
Think of it as a centralized link-state algorithm
Switches send connectivity info to controller
Controller computes forwarding state
  Some control program that uses the topology as input
Controller sends forwarding state to switches
Controller is replicated for resilience
  System is only “logically centralized”

## Slide 50: Software Defined Network (SDN)
Control Program
Network OS
Global Network View
Traditional Control Mechanisms
Network of Switches and/or Routers
Distributed algorithm running between neighbors
Complicated task-specific distributed algorithm
routing, access control, etc.

## Slide 51: Major Change in Paradigm
Control program: Configuration = Function(view)
  Configuration means set of forwarding entries
Control mechanism now program using NOS API
Not a distributed protocol, just a graph algorithm
Configurations are passed to switches by NOS

## Slide 52: Software Defined Network (SDN)
Control Program
Network OS
Global Network View
routing, access control, etc.

## Slide 53: Questions?

## Slide 54: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration
  Otherwise, control program must compute forwarding entries for every switch in network….

## Slide 55: Abs#3: Specification Abstraction
Control mechanism expresses desired behavior
  Whether it be isolation, access control, or QoS
It should not be responsible for implementing that behavior on physical network infrastructure
  Requires configuring the forwarding tables in each switch
Proposed abstraction: abstract view of network
  Abstract view models only enough detail to specify goals
  Will depend on task semantics

## Slide 56: Simple Example: Access Control
Global
Network View
Abstract Network
View
A
B
A
B

## Slide 57: Software Defined Network
Network OS
Global Network View
Abstract Network View
Control Program
Virtualization Layer

## Slide 58: Clean Separation of Concerns
Control program: express goals on abstract view
  Driven by Operator Requirements
Virt. Layer: abstract view  global view
  Implements goals on network (as in global view)
  Driven by Specification Abstraction for particular task
NOS: global view  physical switches
  API: driven by Network State Abstraction
  Switch interface: driven by Forwarding Abstraction

## Slide 59: SDN: Layers for the Control Plane
Network OS
Global Network View
Abstract Network View
Control Program
Virtualization Layer

## Slide 60: Another Separation
SDN separates control and data planes
  SDN platform does control plane
  Switches/routers do data plane
Today’s switches/routers do both
  Requiring standardized control planes
  Or vendor lock-in
Better off separating control and data planes
  So that one can reason globally about control plane
  And have independent data plane implementations

## Slide 61: Completely Changes Ecosystem!
We could go from vertically integrated solutions…
  Proprietary HW and SW sold by big vendors
…to regime like current computational ecosystem
  Commodity hardware (using broadcom and similar chips)
  Third-party and open-source software
Good for....
  Providers
  Users
  Research
  Understanding

## Slide 62: Abstrns Don’t Remove Complexity
NOS, Virtualization are complicated pieces of code
SDN merely localizes the complexity:
  Simplifies interface for control program (use-specific)
  Pushes complexity into reusable code (SDN platform)
This is the big payoff of SDN: modularity!
  The core distribution mechanisms can be reused
  Control programs only deal with their specific function

## Slide 63: What This Really Means

## Slide 64: Routing Application
Look at graph of network
Compute routes
Give to SDN platform, which passes on to switches
Graph algorithm, not distributed protocol

## Slide 65: Access Control Application
Control program decides who can talk to who
Pass this information to SDN platform
Appropriate ACL flow entries are added to network
  In the right places (based on the topology)
The control program that decides who can talk to whom doesn’t care what the network looks like!

## Slide 66: Why Is SDN Important?
As a design:
  It is more modular, enabling faster innovation
  Control programs become very simple!
As an academic endeavor:
  Provides abstractions that enable systematic reasoning
  Can reason about control program, without looking at each switch…
As a change in the ecosystem:
  Open switch interfaces reduce vendor lock-in
  Massive change, which some vendors are resisting

## Slide 67: Common Questions about SDN?
Is SDN less scalable, secure, resilient,…?
Is SDN incrementally deployable?
Can SDN be extended to the WAN?
Is OpenFlow the right fwding abstraction?

## Slide 68: Common Questions about SDN?
Is SDN less scalable, secure, resilient,…? No
Is SDN incrementally deployable? Yes
Can SDN be extended to the WAN? Yes
Is OpenFlow the right fwding abstraction? No

## Slide 69: Why Did We Do a Startup?
An exercise in speaking truth to power….

## Slide 70: How Did We Get This Deployed?
Get everyone to buy OpenFlow switches
  And then install our control software?
That’s ludicrous. So, how did we do it?
  Without them buying new switching hardware?
  And in some cases not even talking to the networking team at the company….
Don’t look at the next slides.
You have 3 minutes…..go!

## Slide 71: Deployability

## Slide 72: Fact #1
Most functionality can be implemented at edge
  Access control
  Isolation
  ….
Network core merely needs to deliver packets
  Current networking technologies pretty good at this
So only need to add SDN at edge…

## Slide 73: Fact #2
The operators who were crying were from large multitenant datacenters….
They run hypervisors on their hosts, support VMs running for tenants
This gave us an opening….

## Slide 74: Virtualization makes this easy…
Virtualization (VMs) is supported by hypervisors
Hypervisors use software switch to connect VMs
Make this software switch SDN-compatible
  And you’ll be able to deploy SDN without any new HW
Open vSwitch is now in Linux, Xen, etc.
SDN now deployable without any HW deployment!

## Slide 75: Network in Regular Setting
Host
Host
Host
Host
Physical Switch

## Slide 76: Network in Virtualized Setting
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM

## Slide 77: Virtual Switches (Vswitch)
Virtual Switch
VM
VM
VM
VM
Vswitch is first-hop switch for all VMs
  Software switch (speed is not an issue)
  Should support OpenFlow
  Can be controlled by Network Operating System

## Slide 78: Physical View of Virtualized Network
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM
Host
Hypervisor
VM
VM
VM
VM

## Slide 79: Logical View of Virtualized Network
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
All edge switches are Vswitches

## Slide 80: Vswitches are Sufficient
Vswitches are enough to implement most functions
  Access control, QoS, mobility, migration, monitoring,…
Physical network becomes static crossbar
  Simple to implement and manage
  Components can be legacy and static

## Slide 81: Managing Physical Network
NOS
Physical Switches

## Slide 82: Managing Virtualized Network
Physical network is logical crossbar
NOS
Only Vswitches need to be controlled by NOS

## Slide 83: Vswitches as Insertion Point
Can insert new functionality into old networks with
  Hypervisors with OpenFlow-enabled Vswitch
  Network Operating System (on servers)
No change to physical infrastructure
  Legacy hosts
  Legacy network components

## Slide 84: Questions?

## Slide 85: We are done….