## Slide 1: CS 168 Fundamentals of Routing
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Naming is Extremely Important
My name is not Professor Shenker:
  That’s my brother….
My name is not Dr. Shenker
  That was my father…
My name is Scott.
I’m not trying to be one of you, or be your friend…
  I just don’t believe in titles or being formal
But beneath my affable informality…
  I’m still an arrogant and self-centered asshole….

## Slide 4: Thank You
As a class you’ve been great so far.
Engaged
Quiet
Many are distracted by your screens, but enough of you pay attention so I don’t feel like a total failure.
A few of you are asleep by my fourth slide….
  C’mon, fourth slide? Give me a break….

## Slide 5: Reminder
Project due Monday!

## Slide 6: Where Are We?
Wallowing in the shame of failure….
  Exercise did not find a path, any path.
  Worst failure in all my years of teaching this course....
Today’s goals:
  Understand routing
  Reclaim your self-esteem
Assuming destination-based routing (typical case)

## Slide 7: Local vs Global View of State
Local routing state is table in a single router
  By itself, the state in a single router can’t be evaluated
  It must be evaluated in terms of the global context
Global state is collection of tables in all routers
  Global state determines which paths packets take
  (Will discuss later where this routing state comes from)

## Slide 8: “Valid” Routing State
Global routing state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
  Valid is my terminology, not standard
Goal of routing protocols: compute valid state
  But how can you tell if routing state if valid?
Need a succinct correctness condition for routing
  Think about this….what makes routing incorrect?
  Take a few minutes.....
Notes: What could go wrong?

## Slide 9: Necessary and Sufficient Condition
Global routing state is valid if and only if:*
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing port
  A packet arrives, but the forwarding decision does not yield any outgoing port (and that node is not destination)
A loop is when a packet cycles around the same set of nodes forever
NOTE: when a packet is delivered to destination, it is no longer forwarded…

## Slide 10: Packet Hitting Dead End
Packet reaches deadend and stops (and dropped)

## Slide 11: Packet Entering Loop
Packet falls into loop and never reaches destination

## Slide 12
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
MIT | switch#2
NYU | switch#3
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Forwarding Table
switch#1
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Loop!

## Slide 13
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
NYU | switch#3
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Forwarding Table
switch#1
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Deadend (to MIT)

## Slide 14: Necessary and Sufficient Condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
Necessary: (only if)
  If routing state valid, then there are no loops/deadends
Sufficient: (if)
  If no loops/deadends, then routing state is valid
This result holds for any deterministic forwarding state (i.e., need not be destination-based)

## Slide 15: Necessary (“only if”): Easy
If you run into a deadend before hitting destination, you’ll never reach the destination
If you run into a loop, you’ll never reach destination
  With deterministic forwarding, once you loop, you’ll loop forever (assuming routing state is static)
Therefore:
  If routing state valid, then there are no loops/deadends

## Slide 16: Sufficient (“if”): More Subtle
Assume no deadends, no loops, yet not valid
Packet must keep wandering, without repeating
  If ever enter same switch from same port, will loop
  Because forwarding decisions are deterministic
Only a finite number of possible ports for it to visit
  It cannot keep wandering forever without looping
  Must eventually hit destination
Therefore:
  If no loops/deadends, then routing state is valid
Notes: Destination is only safe deadend

## Slide 17: Two Questions
How can we verify given routing state is valid?
How can we produce valid routing state?

## Slide 18: Checking Validity of Routing State
Focus only on a single destination
  Ignore all other routing state (why can we do this?)
For each node, mark outgoing port with arrow
  There can only be one at each node (destination-based)
Eliminate all links with no arrows
Look at what’s left….
  State is valid if and only if remaining graph is spanning tree rooted at destination
  Spanning tree: tree that touches all nodes

## Slide 19: Example 1

## Slide 20: Pick Destination

## Slide 21: Put Arrows on Outgoing Ports (output ports towards green dot)

## Slide 22: Remove Unused Links
Leaves Spanning Tree: Valid

## Slide 23: Second Example

## Slide 24: Second Example
Is this valid?

## Slide 25: Third Example

## Slide 26: Third Example
Is this valid?

## Slide 27: Lesson….
Very easy to check validity of routing state for a particular destination
Deadends are obvious
  Node without outgoing arrow, can’t be connected to dest.
Loops are obvious
  Disconnected from destination (and rest of graph)

## Slide 28: Two Questions
How can we verify given routing state is valid?
How can we produce valid routing state?

## Slide 29: The “Secret” of Routing
Avoiding deadends is easy
Avoiding loops is hard
The key difference between routing protocols is how they avoid loops!
  Don’t focus on details of mechanisms
  Just ask “how are loops avoided?”
Like Tuesday, we will learn-by-doing…
Notes: Most modern routing research is about how to make the loop-freeness a more fundamental part of the algorithm. In what I’m going to present today, it is only loop-free AFTER convergence. That’s not good enough

## Slide 30: Design Exercise: Five Minutes
Talk to people around you
Try to design a way to avoid loops
After five minutes, I will call on a few groups….
Point of exercise not to get the “right answer”!
I want you to think about loop avoidance yourself
  Then the rest of the lecture will make more sense!

## Slide 31: #1: Create Tree Out of Topology
Remove enough links to create a tree topology
If the topology has no loops, then just:
  Make sure that you never send packets back to where they came from (that causes an immediate loop)
Thus, if the topology has no loops, and routing doesn’t do anything locally stupid, routing is valid
First challenge: reduce general topology to a tree!
Second challenge: choose which branches to take
Third challenge: route without pre-installed routing state (no route computation)!

## Slide 32: #2 Obtain a Global View
If I see the entire network, then when computing paths I can explicitly avoid loops
  Many graph algorithms for computing loop-free paths
  You can use any of them….
Simple algorithm:
  For given source, pick an arbitrary path to destination
  For any node not on path, draw a path that does not contradict earlier path
  Continue until all nodes are covered
Challenge is how to get this global view of network

## Slide 33: This Was Approach on Tuesday
Have everyone stand and report their connectivity
Have someone record this data
And then compute a route

## Slide 34: #3 Distributed Route Computation
Approach A: Computation minimizes metric
  Why does this work?
Approach B: Routers explicitly exchange paths
  If the route computation shows the paths being computed, can always avoid creating a loop
  Will explain this later when we get to Interdomain routing

## Slide 35: Realizing Approach A: Shortest Paths
Destination stands up (distance 0)
  Announces neighbors and distance (and then sits down)
Neighbors stand up (distance 1)
  They remember who called them to stand
  They announce their neighbors (distance 2), and sit
These neighbors stand up (if haven’t already)
…..and so on, until source stands
At that point, the source can send a packet to the person who called them to stand, and then recursively the packet can reach the destination….
Notes: Let’s try this again!!!

## Slide 36: This is what you should have done…
And there’s only one way to deal with the shame
  We must try again, and do it live!

## Slide 37: Please Act Out This Algorithm
Destination stands up (distance 0)
  Announces neighbors and distance (and then sits down)
Neighbors stand up (distance 1)
  They remember who called them to stand
  They announce their neighbors (distance 2), and sit
These neighbors stand up (if haven’t already)
…..and so on, until source stands
Why do you not stand up twice?
Notes: Let’s try this again!!!

## Slide 38
1
16
36
7
25
10
19
5
34
38
29
33
15
39
23
14
9
2
35
11
22
32
26
21
37
3
28
12
30
4
27
20
31
18
24
40
8
17
6
13

## Slide 39: Distributed Route Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
I am the
Destination
I am three hops away

## Slide 40: How Robust is This?
What if people don’t go in order?
  Someone who is three hops away stands up before someone who is two hops away?
Must announce the distance when you stand up
If learn shorter path:
  Announce your new distance
  Remember only shortest distance

## Slide 41: This Distributed Process
Finds a path
  In fact, shortest path
Creates the appropriate routing state
  Forward packet to neighbor who has the shortest path
And tells everyone the length of their path

## Slide 42: #3 Distributed Route Computation
Approach 1: Computation minimizes metric
  Why does this work?
  Why does it have to be minimize?
Approach 2: Routers explicitly exchange paths
  If the route computation shows the paths being computed, can always avoid creating a loop
  Will explain this later when we get to Interdomain routing

## Slide 43: Realizing Approach B
Destination stands up
  Announces existence to selected neighbors (and path)
Neighbors stand up
  They remember path, and add themselves to path
  Announce path to selected neighbors, and sit
These neighbors
  Decide whether to choose path (but never create loop)
  If they choose this new path, they
    Add themselves to path
    Announce path to selected neighbors
Neighbors only announce when they select a new path (or want to remind their neighbor)…..
Notes: Let’s try this again!!!

## Slide 44: Ways to Avoid Loops (Conceptual)
Create a tree-like topology
  If the topology has no loops, you can’t create them
  (Unless you are locally stupid!)
Create a global view, then use graph algorithm
  If I see the entire network when computing paths I can manually avoid loops
Distributed Computation:
  Routes that minimize some metric
  Computations that show me the path that I’m choosing

## Slide 45: Ways to Avoid Loops (In Practice)
Tree-like topologies
  Learning switches (L2)
Global view
  Link-state and SDN routing
Distributed Computation:
  Minimizing a metric: Distance vector
  Showing path: BGP
  Represents essentially all routing algorithms….
Notes: There are other properties one wants in routing algoirithms (instant recovery from failures), and that goes beyond what we are doing….

## Slide 46: Where Are These Approaches Used?
Local-Area-Networks (LANs): typically L2
  Scope: Single buildings (or even floors of buildings)
  Routing approach: Spanning Tree plus Learning
  Technology: Ethernet
Enterprise and Carrier Networks: intradomain
  Scope: campus to global, but within single domain
  Routing approach: global view or distributed metric
  Protocols: OSPF (g. view) or RIP (minimize hop count)
Interdomain routing (the highest level)
  Scope: global, between domains
  Routing approach: distributed (path vector)
  Protocol: BGP

## Slide 47: Rest of Lecture
Tackling spanning trees at an abstract level
Will talk about the details of all three approaches next week (end of routing)

## Slide 48: Easiest Way to Avoid Loops
Use a topology where loops are impossible!
Take arbitrary topology
Build spanning tree
  Ignore all other links
Only one path to destinations on spanning trees

## Slide 49: How Do You Make Spanning Trees?
The Spanning Tree Protocol (STP)
  Invented by Radia Perlman
  Used to link together Ethernets in the early Internet
How does it work?
  Pick lowest ID in network as root
    This is pretty easy…
  Build tree rooted in that node
    Using techniques similar to routing
Will cover protocol later in lecture (or next time)

## Slide 50: Consider previous graph

## Slide 51: A Spanning Tree

## Slide 52: Another Spanning Tree

## Slide 53: Yet Another Spanning Tree

## Slide 54: How To Route on Spanning Tree?
There is only one path from source to destination
How do you find that path? Ideas?
Easy to design routing algorithms for trees
  When a node “flood” packet to all other nodes
  All routers can then establish routing state for that node
Why bother? Just flood with no routing state
  Flood delivers a packet to destination
  No packets will loop, but most will hit deadends
  But one (and exactly one) will reach destination

## Slide 55: Flooding on a Spanning Tree
If you want to send a packet that will reach all nodes, then switches can use the following rule:
  Ignoring all ports not on spanning tree!
Originating switch sends “flood” packet out all ports
When a “flood” packet arrives on one incoming port, send it out all other ports

## Slide 56: Flooding on Spanning Tree

## Slide 57: Flooding on Spanning Tree (Again)

## Slide 58: Flooding on a Spanning Tree
This works because the lack of loops prevents the flooding from cycling back on itself
Eventually all nodes will be covered, exactly once
So one copy of the packet will be delivered to destination.

## Slide 59: But isn’t flooding wasteful?
Yes, but you can watch the packets going by, and learn from that (so not all future packets flooded)
There is a single path between any two nodes
If node A sees a packet sent from node B to node C, what can it conclude?
  Does it now know how to reach C?
  Does it now know how to reach B?
It knows what port to use to reach B!

## Slide 60: Nodes can “learn” routing tables
Switch can learn how to reach nodes by remembering where flooding packets came from!
If flood packet from Node A entered switch from port 4, then switch uses port 4 to reach Node A
Until a node sends a packet, packets sent to it are flooded, but afterwards they can be routed

## Slide 61: Learning from Flood Packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 62: Node B Responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 63: General Approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded
The decision to flood or not is done on a switch-by-switch basis….

## Slide 64: Self-Learning Switch
When a packet arrives
Inspect source ID, associate with incoming port
Store mapping in the switch table
Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 65: Self Learning: Handling Misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response will teach switch about that destination
A
B
C
D

## Slide 66: General Rule
When switch receives a packet:
index the switch table using destination ID
if entry found for destination {
if dest on port from which packet arrived then drop packet
else forward packet on port indicated
}
else flood
forward on all but the interface
on which the frame arrived
Why do this?

## Slide 67: Summary of Learning Approach
Avoids loop by restricting to spanning tree
This makes flooding possible
Flooding allows packet to reach destination
And in the process switches learn how to reach source of flood
No explicit route “computation”

## Slide 68: When Is This Approach Useful?
When nodes are coming and going….
No need to compute routing state beforehand
Use flood for initial deliveries, and then learn how to reach based on responses
Only need forwarding state for active hosts
We call this “plug-and-play”!
  Used in L2

## Slide 69: Next Week
Detailed protocols for various routing algorithms
Boring beyond belief….
…but there will be poetry
Radia Perlman writes an ode to spanning trees
And Murphy McCauley destroys them with a blistering diss track….

## Slide 70: Spanning Tree Protocol (Perlman‘85)
Protocol by which bridges construct a spanning tree
  Used to link together Ethernets in the early Internet
Key property: Zero configuration
  By operators or users (plug-and-play)
Still used today (with switches)

## Slide 71: Algorithm Has Two Aspects
Pick a root:
Destination to which shortest paths go
Pick the one with the smallest identifier
Compute shortest paths to the root:
No shortest path can have a cycle
Only keep the links on shortest-paths
  Break ties in some way if multiple shortest paths
Voila, a spanning tree!
Spanning Tree Protocol does both with single algorithm

## Slide 72: Breaking Ties
When there are multiple shortest paths to the root, choose the path that uses the neighbor switch with the lower ID.
One could use any tiebreaking system, but this is an easy one to remember and implement
  And please do remember it….

## Slide 73: First Trees, then Protocol
Will first show you which trees result from:
  Pick smallest ID as root
  Create shortest-path tree rooted at this node
  Break ties by favoring lowest ID neighbor
Will then show you a protocol that does this…

## Slide 74: Graph: what is the spanning tree?
1
2
3
4
5
6
7

## Slide 75: Links on spanning tree
Node 1 is root
3-1
5-1
6-1
2-3
4-2
7-2
1
2
3
4
5
6
7

## Slide 76: Node 1 Dies….what is tree now?
2
3
4
5
6
7

## Slide 77: Resulting Spanning Tree
2 is new root
3-2
6-2
4-2
7-2
5-6
2
3
4
5
6
7

## Slide 78: Constructing a Spanning Tree
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And advertising a distance d to Y
Switch selects node with smallest ID as root
  Y in the messages (smallest switch has seen so far)
  Initially different nodes have different ideas about root
Switch discards links not on shortest path to root
  Based on d to Y in the messages

## Slide 79: Intuition
Only pay attention to messages with the smallest value of Y (root)
Only pay attention to messages with the smallest value of d for that root
Only pay attention to shortest path with lowest switch ID

## Slide 80: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  I.e., switch X announces (X, 0, X) to its neighbors
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If Y’s id < current root: set root = Y
Switches compute their distance from the root
  Add 1 to the shortest distance received from a neighbor
If root or shortest distance to it changed, send neighbors updated message (Y, d+1, X)

## Slide 81: Example (root, dist, from)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(3,0,3)
(4,0,4)
(5,0,5)
(6,0,6)
(7,0,7)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(1,3,4)
(1,1,5)
(1,1,6)
(1,3,7)
✗
✗
✗

## Slide 82: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 83: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 84: Robustness of Algorithm
Algorithm must react to failures
  Failure of the root node
  Failure of other switches and links
Root switch sends periodic messages
  These declare itself as root
  Other switches forward messages in response
Detecting failures through timeout
  If no word from root, time out and claim to be the root!

## Slide 85: Example of Self-Stabilizing Algorithm
No matter how what the initial condition is
  State of links
  State in switches
If no additional failures/recoveries, then eventually the algorithm will converge to the right answer…
Requires:
  “Soft state”: state that times out if not refreshed
  “Always in recovery”: Constantly recomputing

## Slide 86: An Ode to STP
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
is loop-free connectivity.
A tree that must be sure to span
so packets can reach every LAN.
First, the root must be selected.
By ID, it is elected.
Least-cost paths from root are traced.
In the tree, these paths are placed.
A mesh is made by folks like me,
Then bridges find a spanning tree.

## Slide 87: Weaknesses of This Approach?
Requires loop-free topology (Spanning Tree)
  Must eliminate many links from physical topology
  Reducing bisection bandwidth (important in datacenters)
  Very little control over paths (traffic engineering)
Slow to react to failures
  Tree must be recomputed
Slow to react to host movement
  Entries must time out
Spanning Trees suck (just ask an operator)

## Slide 88: Murphy’s Research (AXE)
Do flooding without a spanning tree
  By having routers detect duplicates
Eliminates most weaknesses of this approach
  No need to eliminate links
  Can recover from failures immediately
  ….

## Slide 89: Murphy’s Diss Track
I think that I shall never see
a structure more wasteful than a tree.
Most links remain idle and unused
while others are overloaded and abused.
And with each failure comes disruption
caused by the ensuing tree construction.
Thus, L2 must discard its spanner,
requiring flooding in a different manner.
For the tree’s fragile waste to be abated,
trim no branches and detect packets duplicated.
Notes: Our version of Drake vs Meek Mill