## Slide 1: CS 168 More Detailed Discussion of Routing: Part I (the easy stuff)
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Announcement
No office hours today
Office hours Thursday 7:00-8:00

## Slide 4: Warning
I will occasionally talk about nontechnical topics
  Typically at the beginning of lecture
  Often remarks I’ve given elsewhere
Such as:
  What I said at my advisor’s memorial
  My commencement address
  ...
Why?
  Because there is more to life than networking
  And CS is the least important thing I do in my life
    Aside from ping pong…

## Slide 5: Ways to Avoid Loops (Conceptual)
Create a tree-like topology
  If the topology has no loops, you can’t create them
  (Unless you are locally stupid!)
Create a global view, then use graph algorithm
  If I see the entire network when computing paths I can manually avoid loops
Distributed Computation:
  Routes that minimize some metric
  Computations that show me the path that I’m choosing

## Slide 6: Ways to Avoid Loops (In Practice)
Tree-like topologies
  Learning switches (L2)
Global view
  Link-state and SDN routing
Distributed Computation:
  Minimizing a metric: Distance vector
  Showing path: BGP (path vector)
  Represents essentially all routing algorithms….
Notes: There are other properties one wants in routing algoirithms (instant recovery from failures), and that goes beyond what we are doing….

## Slide 7: Today’s Lecture
Global View: Link-state
Tree-like topologies: Learning switches and STP
  STP = Spanning Tree Protocol
Notes: There are other properties one wants in routing algoirithms (instant recovery from failures), and that goes beyond what we are doing….

## Slide 8: Next Lecture
Distributed computations (detailed)
  Distance Vector
  Path Vector
Comparisons:
  Where to use certain routing algorithms

## Slide 9: Ground Rules for Today
This is the first algorithmic content….
  Not deep at all
  But you might not follow all the details
Ask questions!
  To fill in holes
  To clarify confusion
  To slow me down!
I deliberately cut down length of lecture to allow Qs

## Slide 10: Global View

## Slide 11: Two Aspects to Global View Method
Algorithm: computing loop-free paths on graph
  Straightforward to compute lowest-cost paths
  We won’t waste any time on this
Protocol: What we focus on today
  Where to create global view
  How to create global view
  Disseminating the route computation (if necessary)
  When to run route computation

## Slide 12: First Protocol Decision
Where to create global view?
  Centralized server (which then disseminates routes)
    SDN: later in course
  In every router (no need to disseminate routes)
    Link-state routing: what we will cover now
Link-state routing
  OSPF is a link-state protocol
    IETF RFC 2328 (IPv4) or 5340 (IPv6)
  OSPF used at Berkeley

## Slide 13: Routing “Metrics”
Classroom alg. finds path with smallest hop-count
  If properly implemented….
Other routing goals (besides hop-count)
  Path with lowest latency
  Path with the least load
  Path with most reliable links
  ….
Generally, assume every link has “cost” associated with it, and you want to minimize the cost of the entire path

## Slide 14: Overview of Link State Routing
Every router knows its local “link state”
  Knows state of links to neighbors
  Up/down, and associated “cost”
A router floods its link state to all other routers
  Flood: a packet that is delivered to all nodes (next slide)
  Hence, every router learns the entire network graph
Runs route computation locally
  Computing least-cost paths from them to all other nodes

## Slide 15: How Does Flooding Work?
Packet arrives on port at switch
That switch:
  Remembers the packet
  Forwards packet out all other ports
  Does not send it out the incoming port
If a previously received packet arrives again…
  Router drops it (no need to forward again)

## Slide 16: Link State Routing
First each router floods their link state
Routers remember which updates they’ve seen, so they don’t resend them….
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 17: Then Each Node Has Global View
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C

## Slide 18: When to Initiate Flood?
Topology change
  Link or node failure (looks the same to the router)
  Link or node recovery (ditto)
Configuration change
  Link cost change (why would one change link cost?)
Periodically
  Refresh the link-state information
  Typically (say) 30 minutes
  Corrects for possible corruption of the data

## Slide 19: Making Flooding Reliable
Reliable flooding
  Ensure all nodes receive link-state information
  Ensure all nodes use the latest version
Solutions in Reliable Transport lectures
How can it still fail?
Can you ever have loops with link-state routing?
Notes: When node goes down, it might take an update with it…..and then come back up and not remember it.

## Slide 20: Are Loops Still Possible?
A and D think that this is the path to C
E thinks that this is the path to C
A
E
D
C
B
F
A
E
D
C
B
F
1
3
1
1
5
5
5
5
5
E-C link fails, but
D doesn’t know yet
E reaches C via D
D reaches C via E
Loop!

## Slide 21: Transient Disruptions
Inconsistent link-state views
  Some routers know about failure before others
  The shortest paths are no longer consistent
  Can cause transient forwarding loops
A
E
D
C
B
F
A
E
D
C
B
F
A and D think that this is the path to C
E thinks that this is the path to C
Loop!

## Slide 22: “Convergence”
All routers have consistent routing information
  E.g., all nodes having the same link-state database
Forwarding is consistent after convergence
  All nodes have the same link-state database
  All nodes forward packets on same paths
But while still converging, bad things can happen

## Slide 23: Time to reach convergence
Sources of convergence delay?
  Time to detect failure
  Time to flood link-state information (~longest RTT)
  Time to re-compute forwarding tables
Performance problems during convergence period?
  Deadends
  Looping packets
  Out-of-order packets reaching the destination
    Should not cause semantic problems
    But can create performance problems!

## Slide 24: Timeline for Local Failure
Failure not detected: packets go into dead link
Detected, not recomputed: packets dropped
  Deadends
  This is where precomputed failovers would help
Detected/computed, not globally notified/computed
  Could be loops
As nodes become aware, routes may change
  Continued looping, and possible reorderings
  Why reordering?

## Slide 25: Link-State is conceptually simple
Everyone floods link information
Everyone then knows map of network
Everyone independently computes paths on map
All the complexity is in the details

## Slide 26: Tree-like Topologies
Come for the routing
Stay for the poetry…

## Slide 27: Two Challenges for Tree Topologies
Take arbitrary topology, turn into spanning tree
  By eliminating some links
Devise way to route on spanning tree
  How do you ensure delivery?
We will start with the second challenge first.
  But first, what is a spanning tree?

## Slide 28: Consider general graph

## Slide 29: A Spanning Tree

## Slide 30: Another Spanning Tree

## Slide 31: Yet Another Spanning Tree

## Slide 32: How To Route on Spanning Tree?
There is only one path from source to destination
How do you find that path? Ideas?

## Slide 33: Flooding!
Flooding a packet means sending it to all nodes
When a node “floods” packet to all other nodes
  All routers can then establish routing state for that node
  Because they know where to find that node
But note: flooding also delivers packets!
  So why bother with a routing protocol?
  When you don’t know route, just flood.
  Flood delivers a packet to destination
  No packets will loop, and most will hit deadends
  But one (and exactly one) will reach destination

## Slide 34: Flooding on a Spanning Tree
If you want to send a packet that will reach all nodes, then switches can use the following rule:
  Ignoring all ports not on spanning tree!
Originating switch sends “flood” packet out all ports
When a “flood” packet arrives on one incoming port, send it out all other ports

## Slide 35: Flooding on Spanning Tree

## Slide 36: Flooding on Spanning Tree (Again)

## Slide 37: Question
Do switches need to remember flooded packets?
Remember, for link-state the flooding algorithm required routers to remember packets
  And not resend them
Do we need to do that here?
Why is this important?
  Link-state: routing messages are flooded
  Learning: regular traffic can be flooded!

## Slide 38: Flooding on a Spanning Tree
This works because the lack of loops prevents the flooding from cycling back on itself
Eventually all nodes will be covered, exactly once
So one copy of the packet will be delivered to destination.
But isn’t flooding wasteful?

## Slide 39: Flooding Yields Information
Floods do waste bandwidth, but you can watch the packets going by, and learn from that
  So not all future packets flooded…
There is a single path between any two nodes
If node A sees a packet sent from node B to node C, what can it conclude?
  Does it now know how to reach C?
  Does it now know how to reach B?
It knows what port to use to reach B!

## Slide 40: Nodes can “learn” routing tables
Switch can learn how to reach nodes by remembering where packets came from!
If packet from Node A entered switch from port 4, then switch uses port 4 to reach Node A
Until node A sends a packet, packets sent to node A are flooded, but afterwards they can be routed
  Before node A sends a packet, no routing state for it
  But after node A sends a packet, some routing state

## Slide 41: Learning from Flood Packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 42: Node B Responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 43: General Approach
Send packet to destination
  If no routing state for destination, then packet is flooded
If flood: all switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded

## Slide 44: Bandwidth Tradeoff
Every time new node arrived, it could send a flood packet so that all routers knew where it was.
But if:
  Nodes come and go often
  Many nodes don’t have packets sent to them
Then such messages are wasted.
The flood and learn approach only sets up routing state for nodes that are active

## Slide 45: But I need to clear something up…
The decision to flood or not is done on a switch-by-switch basis….
Packets are not either flooded or point-to-point
Instead, at each switch, packets are:
  Sent out correct port if switch has routing state
  Flooded out all ports (except incoming) if switch does not have routing state

## Slide 46: Self-Learning Switch
When a packet arrives
Inspect source ID, associate with incoming port
Store mapping in the switch table
Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 47: Self Learning: Handling Misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response will teach switch about that destination
A
B
C
D

## Slide 48: General Rule
When switch receives a packet:
index the switch table using destination ID
if entry found for destination {
if dest on port from which packet arrived then drop packet
else forward packet on port indicated
}
else flood
forward on all but the interface
on which the frame arrived
Why do this?

## Slide 49: Reviewing the Process
A sends packet to B:
  Any routers handling packet learns where A is
  Can establish routing state for A
When B responds, can follow routing state to A
  Any routers handling packet learns where B is
Nodes that are “silent” have no routing state

## Slide 50: Summary of Learning Approach
Avoids loop by restricting to spanning tree
This makes flooding possible
Flooding allows packet to reach destination
And in the process switches learn how to reach source of flood
No explicit route “computation”

## Slide 51: Creating Spanning Trees

## Slide 52: Spanning Tree Protocol (Perlman‘85)
Protocol by which bridges construct a spanning tree
  Used to link together Ethernets in the early Internet
Key property: Zero configuration
  By operators or users (plug-and-play)
Still used today (with switches)

## Slide 53: Algorithm Has Two Aspects
Pick a root:
Destination to which shortest paths go
Pick the one with the smallest identifier
Compute shortest paths to the root:
Collection of shortest paths (to root) cannot have cycle
Only keep the links on shortest-paths
  Break ties in some way if multiple shortest paths
Voila, a spanning tree!
Spanning Tree Protocol does both with single algorithm

## Slide 54: Breaking Ties
When there are multiple shortest paths to the root, choose the path that uses the neighbor switch with the lower ID.
One could use any tiebreaking system, but this is an easy one to remember and implement
  And please do remember it….

## Slide 55: First Trees, then Protocol
Will first show you which trees result from:
  Pick smallest ID as root
  Create shortest-path tree rooted at this node
  Break ties by favoring lowest ID neighbor
Will then show you a protocol that does this…

## Slide 56: Graph: what is the spanning tree?
1
2
3
4
5
6
7

## Slide 57: Links on spanning tree
Node 1 is root
3-1
5-1
6-1
2-3
4-2
7-2
1
2
3
4
5
6
7

## Slide 58: Node 1 Dies….what is tree now?
2
3
4
5
6
7

## Slide 59: Resulting Spanning Tree
2 is new root
3-2
6-2
4-2
7-2
5-6
2
3
4
5
6
7

## Slide 60: Spanning Tree Protocol
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And advertising a distance d to Y
Switch selects node with smallest ID as root
  Y in the messages (smallest switch has seen so far)
  Initially different nodes have different ideas about root
Switch discards links not on shortest path to root
  Based on d to Y in the messages

## Slide 61: Intuition
Messages (Y, d, X)
Only pay attention to messages with the smallest value of Y (root)
Only pay attention to messages with the smallest value of d for that root
Only pay attention to shortest path with lowest switch ID (X in message)

## Slide 62: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  I.e., switch X announces (X, 0, X) to its neighbors
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If Y’s id < current root: set root = Y
Switches compute their distance from the root
  Add 1 to the shortest distance received from a neighbor
If root or shortest distance to it changed, send neighbors updated message (Y, d+1, X)

## Slide 63: Example (root, dist, from)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(3,0,3)
(4,0,4)
(5,0,5)
(6,0,6)
(7,0,7)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(1,3,4)
(1,1,5)
(1,1,6)
(1,3,7)
✗
✗
✗

## Slide 64: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 65: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 66: Robustness of Algorithm
Algorithm must react to failures
  Failure of the root node
  Failure of other switches and links
Root switch sends periodic messages
  These declare itself as root
  Other switches forward messages in response
Detecting failures through timeout
  If no word from root, time out and claim to be the root!

## Slide 67: Example of Self-Stabilizing Algorithm
No matter how what the initial condition is
  State of links
  State in switches
If no additional failures/recoveries, then eventually the algorithm will converge to the right answer…
Requires:
  “Soft state”: state that times out if not refreshed
  “Always in recovery”: Constantly recomputing

## Slide 68: Field was designing algorithms…
But then a poetry slam broke out!

## Slide 69: An Ode to STP
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
is loop-free connectivity.
A tree that must be sure to span
so packets can reach every LAN.
First, the root must be selected.
By ID, it is elected.
Least-cost paths from root are traced.
In the tree, these paths are placed.
A mesh is made by folks like me,
Then bridges find a spanning tree.

## Slide 70: Weaknesses of This Approach?
Requires loop-free topology (Spanning Tree)
  Must eliminate many links from physical topology
  Reducing bisection bandwidth (important in datacenters)
  Very little control over paths (traffic engineering)
Slow to react to failures
  Tree must be recomputed
Slow to react to host movement
  Entries must time out
Spanning Trees suck (just ask an operator)

## Slide 71: Murphy’s Research (AXE)
Do flooding without a spanning tree
  By having routers detect duplicates
Eliminates most weaknesses of this approach
  No need to eliminate links
  Can recover from failures immediately
  ….

## Slide 72: Murphy’s Diss Track
I think that I shall never see
a structure more wasteful than a tree.
Most links remain idle and unused
while others are overloaded and abused.
And with each failure comes disruption
caused by the ensuing tree construction.
Thus, L2 must discard its spanner,
requiring flooding in a different manner.
For the tree’s fragile waste to be abated,
trim no branches and detect packets duplicated.
Notes: Our version of Drake vs Meek Mill