## Slide 1: CS 168 Designing IP
Fall 2017
Scott Shenker
CS168.io

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Reminder
LOST Session: Kevin Ma
5:00pm-6:00pm Fridays (Soda 320)
It is not the normal section material
No project questions
But if you are struggling, please do attend….

## Slide 4: Free Speech Week
Our T class conflicts with a talk by David Horowitz
  And possibly Pam Geller
We will have class during Free Speech week
  And you will be responsible for any missed content
However, at end of Tuesday’s lecture, I will make remarks of a political (but nonpartisan) nature
This is a reprise of the commencement address I gave in May to L&S CS majors.
  ~10 minutes

## Slide 5: Agenda for Today
Finish off reliable transport
  Review
  One final observation
Discuss the design of IP

## Slide 6: Complete Correctness Condition
A transport mechanism is “reliable” if and only if
(a) it resends all dropped or corrupted packets
(b) it attempts to make progress

## Slide 7: Solution for the single packet case
Send packet
Set timer
If no ACK when timer goes off, resend packet
  And reset timer
This is “correct”
  Does send initial packet
  Does retry when packet is dropped or corrupted

## Slide 8: General Multipacket Solution
Window-based flow control separates concerns
  Size of W:
  Nature of feedback:
  Response to loss:
Can design each aspect relatively independently
Can be correct, efficient, timely, and fair

## Slide 9: Many Implementation Choices
Feedback from receiver: ACKs vs NACKs
  Can NACKs alone achieve “correctness”?
  Can ACKs alone achieve “correctness”?
Variations on ACKs
  Full information
  Individual packets
  Cumulative (TCP)
When to resend
  Timeout
  Arrival of subsequent packets
  NACKs

## Slide 10: Implementation Choices
These implementation choices affect:
  Timeliness
  Efficiency
  Fairness
  ….
These are important concerns
  but correctness is more fundamental
Design must start with correctness
  Can then “engineer” its performance with various hacks
  These hacks can be “fun” but don’t let them distract you

## Slide 11: Possible Design for Reliable Trans.
Full information ACKs
Window-based, with retransmissions after:
  Timeout
  K subsequent ACKs
This is correct, timely, efficient

## Slide 12: Are We Done?
Are there other approaches?
Suggestions?
What assumption did we make?

## Slide 13: An Implicit Assumption
Delivering the data meant delivering every packet
This assumption built into definition of correctness
But is there another way?

## Slide 14: Alternate Strategy: Rateless Codes
Use special encoding
  Receipt of any set of M packets allows you to recover file
  Where M is close to the size of the original file
Receiver only sends ACK when M are received
  Sender keeps sending until receives ACK
Timely, Correct
  How efficient is it?
  It wastes BxRTT on every flow. Isn’t that awful?

## Slide 15: The Paradox of Internet Traffic
The majority of flows are short
  A few packets
The majority of bytes are in long flows
  MB or more
And this trend is accelerating…

## Slide 16: Inefficiency
The wasted bandwidth ~ BxRTT
For long flows, this is small compared to total file
For short flows, this is large compared to file
  But most of the bandwidth is in long flows!
This is not a terrible idea

## Slide 17: Questions?

## Slide 18: Finished w/ Conceptual Foundations
The basic context and design principles
The fundamental technical challenges
  Routing
  Reliable transport
We now move to the detailed designs in use today
  And we start with IP, the centerpiece of the architecture

## Slide 19: The hardest challenge of all…
Staying awake in lecture on the IP packet header
This is boring stuff, if you only focus on details
But please focus on the following:
  What problems were they trying to address?
  How would you handle them?
All of you are capable of “deriving” IP
  Let’s try to do it together….

## Slide 20: The Design of IP

## Slide 21: What is “designing” a protocol?
Specifying the syntax of its messages
  Format (zzzzzzzz….)
Specifying their semantics
  Meaning
  Responses

## Slide 22: What is Designing IP?
Syntax: format of packet
  Nontrivial part: packet “header”
  Rest is opaque payload (why opaque?)
Semantics: meaning of header fields
  Required processing
Header
Opaque Payload

## Slide 23: Packet Header as Interface
Think of packet header as interface
  Only way of passing information from packet to switch
Designing interfaces:
  What task are you trying to perform?
  What information do you need to accomplish it?
Header reflects information needed for basic tasks

## Slide 24: How Would You Design IP Header?
Take a few minutes to think about this
Talk to your neighbors
Think about:
  What tasks does the header need to perform?
  What information does it need to perform them?

## Slide 25: What Tasks Do We Need to Do?
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 26: Reading Packet Correctly
Where does header end?
Where does packet end?
What version of IP?
  Why is this so important?

## Slide 27: Getting to the Destination
Provide destination address (duh!)
Should this be location or identifier (name)?
  And what’s the difference?
If a host moves, should its address change?
  If not, how can you build scalable Internet?
  If so, then what good is an address for identification?

## Slide 28: Getting Response Back to Source
Source address (duh!)
Other ways for destination to get back to source
  Source address can be in packet payload
  So you could eliminate source address for this reason
But source address is necessary for routers to respond to source with errors

## Slide 29: Carry Data
Payload (duh!)

## Slide 30: Questions?

## Slide 31: List of Tasks
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 32: Telling Dest’n How to Process Packet
Indicate which protocols should handle packet
What layer should this protocol be in?
What are some options for this today?
How does the source know what to enter here?

## Slide 33: Special Handling
Type-of-service: Priority, etc.
Options: discuss later

## Slide 34: Dealing with Problems
Is packet caught in loop?
  TTL
Header Corrupted:
  Detect with Checksum
  What about payload checksum?
Packet too large?
  Deal with fragmentation
  Split packet apart
  Keep track of how to put together

## Slide 35: Are We Missing Anything?
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 36: From Semantics to Syntax
The past few slides discussed the kinds of information the header must provide
Will now show the syntax (layout) of IPv4 header, and discuss the semantics in more detail

## Slide 37: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 38: 20 Bytes of Standard Header, then Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 39: Next Set of Slides
Mapping between tasks and header fields
Each of these fields is devoted to a task
Let’s find out which ones, and why….

## Slide 40: Go Through Tasks One-by-One
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 41: Reading Packet Correctly
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits

## Slide 42: Fields for Reading Packet Correctly
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 43: Getting Packet to Destination and Back
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique locator for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique locator for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source

## Slide 44: Fields for Packet Reaching Destination
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 45: Questions?

## Slide 46: List of Tasks
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 47: Telling Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for demultiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17

## Slide 48: Field for Next Protocol
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 49: Special Handling
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
  Has been redefined several times, no general use
Options
  Ability to specify other functionality
  Extensible format (later)

## Slide 50: Fields for Special Handling
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 51: Option Field Layout
Field | Size (bits) | Description
Copied | 1 | Set if field copied to all fragments
Class | 2 | 0=control, 2=debugging/measurement
Number | 5 | Specifies option
Length | 8 | Size of entire option
Data | Variable | Option-specific data

## Slide 52: Examples of Options
Record Route
Strict Source Route
Loose Source Route
Timestamp
Traceroute
Router Alert
…..

## Slide 53: Potential Problems
Header Corrupted: Checksum
Loop: TTL
Packet too large: Fragmentation

## Slide 54: Preventing Loops
Forwarding loops cause packets to cycle forever
  As these accumulate, eventually consume all capacity
Time-to-Live (TTL) Field (8 bits)
  Decremented at each hop, packet discarded if reaches 0
  …and “time exceeded” message is sent to the source
    Using “ICMP” control message; basis for traceroute

## Slide 55: TTL Field
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 56: Header Corruption
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
  Why include TTL?
  Why only header?

## Slide 57: Checksum Field
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 58: Fragmentation
Every link has “Maximum Transmission Unit” (MTU)
  largest number of bits it can carry as one unit
A router can split a packet into multiple “fragments” if the packet size exceeds the link’s MTU
Must reassemble to recover original packet

## Slide 59: Example of fragmentation
A 4000 byte packet crosses a link w/ MTU=1500B
4000B
1500B
…

## Slide 60: Example of fragmentation
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
A 4000 byte packet crosses a link w/ MTU=1500B
IP header

## Slide 61: Why reassemble?
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
IP header
20
TCP
TCP
TCP
HTTP
HTTP
HTTP
Must reassemble before sending the packet to the higher layers!

## Slide 62: A few considerations
Where to reassemble?
Fragments can get lost
Fragments can follow different paths
Fragments can get fragmented again

## Slide 63: Where Should Reassembly Happen?
Answer 1: router R2
1000
500
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000

## Slide 64: Where should Reassembly Happen?
Answer 2: end-host B (receiver)
500
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000

## Slide 65: Where should reassembly occur?
At next-hop router imposes burden on network
  Complicated reassembly algorithm
  Must hold onto fragments/state
Fragments may take different paths
  So state might not be present for in-network reassembly
Hence, reassembly is done at the destination

## Slide 66: DIY exercise in header engineering
Take 5 minutes to design fragmentation scheme
  Work with your neighbors
At the end of 5 minutes, be ready to tell me:
  How many fields you need?
  What are they and why?
Don’t look for the answer elsewhere, the goal is to think about the problem!

## Slide 67: Reassembly: what fields?
Need a way to identify fragments of the packet
   introduce an identifier
Fragments get reordered?
   need some form of sequence number or offset?
Sequence numbers / offset
  How do I know when I have them all? (need max seq# / flag)
  What if a fragment gets re-fragmented?

## Slide 68: IPv4’s fragmentation fields
Identifier: which fragments belong together
Flags:
  Reserved: ignore
  DF: don’t fragment
    may trigger error message back to sender
  MF: more fragments coming
Offset: portion of original payload this fragment contains
  in 8-byte units

## Slide 69: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 70: Example of Fragmentation
Suppose we have a 4000 byte datagram sent from host 1.2.3.4 to host 3.4.5.6 …
… and it traverses a link that limits datagrams to 1,500 bytes
Version
4
Header
Length
5
Type of Service
0
Total Length: 4000
Identification: 56273
R/D/M
0/0/0
Fragment Offset: 0
TTL
127
Protocol
6
Checksum: 44019
Source Address: 1.2.3.4
Destination Address: 3.4.5.6
(3980 more bytes here)

## Slide 71: Example of Fragmentation (con’t)
Datagram split into 3 pieces
Example:
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320

## Slide 72: Example of Fragmentation, con’t
Datagram split into 3 pieces. Possible first piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1500
Identification: 56273
R/D/M
0/0/1
Fragment Offset: 0
TTL
127
Protocol
6
Checksum: xxx
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 73: Example of Fragmentation, con’t
Possible second piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1220
Identification: 56273
R/D/M
0/0/1
Fragment Offset: 185
(185 * 8 = 1480)
TTL
127
Protocol
6
Checksum: yyy
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 74: Example of Fragmentation, con’t
Possible third piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1320
Identification: 56273
R/D/M
0/0/0
Fragment Offset: 335
(335 * 8 = 2680)
TTL
127
Protocol
6
Checksum: zzz
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 75: Offsets vs Numbering Fragments?
Q: why use a byte-offset for fragments rather than a numbering each fragment?
Ans #1: with a byte offset, the receiver can lay down the bytes in memory when they arrive
Ans #2 (more fundamental): allows further fragmentation of fragments

## Slide 76: IPv6

## Slide 77: IPv6
Motivated (prematurely) by address exhaustion
  Addresses four times as big
Steve Deering focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
  “Spring Cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 78: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 79: Summary of Changes
Eliminated fragmentation (why?)
Eliminated header length (why?)
Eliminated checksum (why?)
New options mechanism (next header) (why?)
Expanded addresses (why?)
Added Flow Label (why?)

## Slide 80: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 81: Philosophy of Changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation
  Eliminated checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header approach)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 82: Comparison of Design Philosophy
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
To Destination and Back (expanded)
Deal with Problems (greatly reduced)
Read Correctly (reduced)
Special Handling (similar)

## Slide 83: We are done for the week….
Have a good weekend